## Slide 1: 课程内容体系
企业生产与运作系统
生产规划
主生产计划
物料需求计划
能力需求计划
生产调度
系统集成体系框架
集散控制系统
生产计划与控制

## Slide 2: Contents for Production Planning and Scheduling
Aggregate Planning
Master Production Schedule
Material Requirement Planning
Capacity Requirement Planning
Purchasing Planning & Shop Planning
Operations scheduling（运作/作业调度）
Project scheduling（项目调度）
Aggregate Planning
Production Planning and Control
Scheduling

## Slide 3
Scheduling：排序，调度，安排时间表，编排进度，编制作业计划

## Slide 4: Scheduling problems
Production scheduling
Personnel scheduling
Facilities scheduling
Vehicle scheduling
Vendor scheduling
Project scheduling
Timetabling
Dynamic vs. static scheduling

## Slide 5: Scheduling Decisions（调度决策）
Organization | Managers Must Schedule the Following
Arnold Palmer Hospital | Operating room use Patient admissions Nursing, security, maintenance staffs Outpatient treatments
HUST | Classrooms and audiovisual equipment Student and instructor schedules Graduate and undergraduate courses
Lockheed-Martin factory | Production of goods Purchases of materials Workers
Hard Rock Cafe | Chef, waiters, bartenders Delivery of fresh foods Entertainers Opening of dining areas
Delta Airlines | Maintenance of aircraft Departure timetables Flight crews, catering, gate, ticketing personnel

## Slide 6: Scheduling Problem
Scheduling concerns optimal allocation or assignment of resources, over time, to a set of jobs, tasks or activities.
Combinatorial optimization problem
Maximize profit
Subject to constraints
Mathematical techniques and heuristics
Job： 工件/任务，被加工的对象，需要完成的任务
Resources： 资源 / 机器 (machine)，对工件进行加工的主体，完 成任务所需要的资源

## Slide 7
Nahmias S. Production and Operations Analysis (7th Edition). 北京: 清华大学出版社, 2018
万国华. 排序与调度的理论、模型和算法. 北京: 清华大学出版社, 2019
Pinedo M. Scheduling Theory, Algorithms and Systems (5th Edition). New York: Springer-Verlag, 2016
刘振元. 服务系统中的多技能人员调度. 北京: 清华大学出版社, 2019
参考书

## Slide 8: 8. 生产调度(Production Scheduling)
8.1 预备知识（Preliminaries）
8.2 机器调度（Machine Scheduling）
8.3 异序作业调度（Job Shop Scheduling）
生产调度

## Slide 9: 8.1 预备知识(Preliminaries)

## Slide 10: Objectives of production scheduling
Meet due dates：满足交货期/截止期
Minimize Work-in-process inventory：最小化在 制品库存
Minimize the average flow time through the system：最小化系统中的平均流时间
Provide for high machine/worker time utilization：提供机器或人员的高利用率
Provide for accurate job status information： 提供精确的工件/任务状态信息
Reduce setup times：减少准备时间
Minimize production and worker costs：最小化 生产和人工成本

## Slide 11: Approach：
Scheduling Problem
Model
Conclusions
Problem Formulation
Solve with Computer Algorithms

## Slide 12: General Solution Techniques
Mathematical programming (数学规划)
  Linear, non-linear, and integer programming
Heuristics (启发式方法)
  Dispatching/prioritizing rules (调度/优先规则)
  Shifting bottleneck heuristic (移动瓶颈法)
  …..
Meta-heuristic/ Local search (元启发式方法/局部搜索)
  Simulated annealing (模拟退火)
  Genetic algorithms (遗传算法)
  Tabu search (禁忌搜索)
  Ant colony optimization (蚁群优化算法)
  ……

## Slide 13: Modeling
Three components to any model:
  Decision variables (决策变量)
    This is what we can change to affect the system, that is, the variables we can decide upon
  Objective function (目标函数)
    E.g, cost to be minimized, quality measure to be maximized
  Constraints (约束)
    Which values the decision variables can be set to

## Slide 14: Decision “Variables”
Three basic types of solutions:
  A sequence(排序): a permutation of the jobs
  A schedule(调度): allocation of the jobs in a more complicated setting of the environment
  A scheduling policy(调度策略): determines the next job given the current state of the system

## Slide 15: Production Scheduling
Production scheduling problems are classified based on machine environment, job characteristics, and optimality criteria.
三元组模型:  |  | 
   machine environment (机器环境)
   job characteristics (工件/任务特征)
   optimality criteria (优化指标)

## Slide 16: Machine Configuration
• Standard machine configurations:
– Single machine models (单机模型)
– Parallel machine models(平行机/并行机模型)
– Flow shop models (流水作业模型)
– Job shop models (异序作业模型)
• Real world always more complicated.

## Slide 17: Machine Configurations
Single Machine
Parallel-Machine
Flow Shop
Job Shop

## Slide 18: Flow shop （流水作业）
In a flow shop each of the n jobs must be processed through the m machines in the same order, and each job is processed exactly once on each machine. This is what we typically think of as an assembly line.

## Slide 19: Job shop （异序作业）
A general job shop differs from a flow shop in that not all jobs are assumed to require exactly m operations, and some jobs my require multiple operations on a single machine. Furthermore, in a job shop each job may have a different required sequencing of operations.
General job shop problems are extremely complex. All purpose solution algorithms for solving general job shop problems do not exist.

## Slide 20: Machine Environment:
Single machine 1
Identical machines in parallel Pm
  If job j may be processed on any one machine belonging to a given subset Mj Pm | Mj | ...
  Machines in parallel with different speeds Qm
  Unrelated machines in parallel Rm
Flow shop Fm
Flexible flow shop FFs
Open shop Om
Job shop Jm
  Job may visit a machine more then once (recirculation) Jm | recrc | ...

## Slide 21: Job Characteristics:
Release time rj：就绪时间，释放时间
Sequence dependent setup times sijk
Preemptions prmp：允许中断
  Preemptive resume
  Preemptive repeat
Precedence constraints prec：先后序关系
Breakdowns brkdwn
Machine eligibility restrictions Mj
Blocking block
No wait no-wait
Recirculation recrc：重复加工
Permutation prmu：同序作业

## Slide 22: Objective/Optimality Criteria:
Throughput (TP) ：产出
Makespan (Cmax)：工期
Due date related objectives：交货期相关目标
Work-in-process (WIP), finished inventory： 在制品，产成品
Lead time (cycle time, response time)：提前期
Others

## Slide 23: Throughput & Makespan
Throughput
  Production rate
  Number of parts produced per time unit
  Defined by bottleneck machines
Makespan
Minimizing makespan tends to maximize throughput

## Slide 24: Due Date Related Objectives
Lateness(延迟)
  Minimize maximum lateness
Tardiness(拖期)
  Minimize total weighted tardiness
Tardy job(拖期任务)
  Minimize the number of tardy jobs

## Slide 25: Due Date Penalties
In practice
Tardiness
Late or Not
Lateness

## Slide 26: Representation Methods
Gantt Chart (甘特图)
Graph (图)

## Slide 27
Machines Mi, i=1,...,m (ith machine)
Jobs Jj, j=1,...,n (jth job)
Schedule may be represented by Gantt charts.
J3
J2
J2
J3
J1
J1
J1
J3
J4
M3
M2
M1
Machine oriented Gantt chart
M1
M2
M2
M1
M3
M3
M2
J1
J2
J3
Job oriented Gantt chart
M1
M1
J4
t
t
Gantt Chart

## Slide 28: Example
Constraints
  Job follows a specific route
  One job at a time on each machine
(1,1)
(2,3)
(3,1)
(4,3)
(1,2)
(1,3)
(2,1)
(2,2)
(4,2)
(3,3)
Machine 1
Machine 2
Machine 3
Machine 4

## Slide 29
Graph Representation
This is a possible schedule:
(Disjunctive arcs，析取弧)
(1,1)
(2,1)
(3,1)
(1,2)
(2,2)
(4,2)
(2,3)
(1,3)
(4,3)
(3,3)
Sink
Source
Graph Representation
Machine constraints must also be satisfied ...

## Slide 30: Complexities of Scheduling Problems
Some scheduling problems are easy
  Simple priority rules
  Complexity: polynomial time
However, most scheduling problems are hard
  Complexity: NP-hard, strongly NP-hard
  Finding an optimal solution is infeasible in practice  heuristic methods

## Slide 31: Algorithm Complexity
Algorithm is bounded
polynomially O(n2)
exponentially O(2n)
Where n is the size of the problem (i.e. number of variables)
NP= set of all problems that can be solved by total enumeration
P= subset of NP consisting of all problems having (known) efficient algorithms (bounded by a polynomial)
NP-hard= subset of NP bounded exponentially
Open= problems in NP but not in P or NP-hard (unknown complexity)

## Slide 32
The efficiency of an algorithm for a given problem is measured by the maximum (worst-case) number of computational steps needed to obtain an optimal solution as a function of the size of the instance.
Problems which have a known polynomial algorithm are said to be in class P. These are problems for which an algorithm is known to exist and it will stop on the correct output while effort is bounded by a polynomial function of the size of the problem.
For NP-hard no simple algorithm yields optimal solutions in a limited amount of computer time.
P & NP-hard problems

## Slide 33: Solution Times
 | n=10 | n=100
O(log n) | 1hr | 2hrs
O(n5) | 1min | 69.4days
O(2n) | 1sec | ?
O(210)= 1 sec
O(2100)= 2100 / 210 sec x 1 min/60sec x 1 hr/60min
x 1 day/24hr x 1 yr/365day x 1 centry/100 yr
= 3.925 x 1017 centuries
The problem is strongly NP-hard!

## Slide 34: Complexity of Job Shop Scheduling problems
n jobs & m machines = (n!)m possible solutions
e.g. 20 x 10 problem => 7.2651x10183 solutions
feasible
solutions
infeasible
solutions

## Slide 35: Combinatorial Optimization
Global Optimum: best solution(s) over the feasibility domain
Local optimum: best solution over some neighborhood
Objective: find a global optimum solution
It may be expensive to find a global optimum

## Slide 36: Optimization algorithms
Conventional optimization algorithms Example Branch & Bound, Integer Linear Programming and Dynamic Programming. works well with small problems slow can’t solve “big” problems
Approximation optimization algorithms Example Dispatching rules, Simulated Annealing, Taboo Search and Genetic Algorithms. fast can be applied with big or small problems approximate “optimal” solutions
Jain et.al. (1999)

## Slide 37: General Solution Techniques
Mathematical programming (not the focus of this course)
  Linear, non-linear, and integer programming
Heuristics
  Dispatching/prioritizing rules
  Shifting bottleneck heuristic
  …..
Meta-heuristic/ Local search (covered in “Production Planning and Scheduling”)
  Simulated annealing
  Genetic algorithms
  Tabu search
  Ant colony optimization

## Slide 38
8.2 机器调度 (Machine Scheduling)

## Slide 39
Machine Scheduling:
Dispatching Rules (调度规则)

## Slide 40: Dispatching Rules
Other names: list scheduling, priority rules
Prioritize all waiting jobs
  job attributes
  machine attributes
  current time
Whenever a machine becomes free: select the job with the highest priority

## Slide 41
Dispatching Rules
Classification
Static: not time-dependent
Dynamic: time dependent
Local: uses information about the queue where the job is waiting or machine where the job is queued
Global: uses information about other machines (e.g. processing time of the jobs on the next machine on its route, or the current queue length)

## Slide 42: Release/Due Date Related
Earliest release date first (ERD) rule
  Variance in throughput times (flow times)
Earliest due date first (EDD) rule
  Maximum lateness
Critical Ratio (CR) rule
  Maximum lateness
  min{(dj-t)/rpj}
Minimum slack first (MS) rule
  Maximum lateness
Current
Time
Processing
Time
Due date
Remaining
Processing
Time

## Slide 43: Processing Time Related
Longest Processing Time first (LPT) rule
  balance load on parallel machines
  makespan
Shortest Processing Time first (SPT) rule
  sum of completion times
  WIP
Weighted Shortest Processing Time first (WSPT) rule

## Slide 44: Other Dispatching Rules
Service in Random Order (SIRO) rule
First In First Out (FIFO)
Shortest Setup Time first (SST) rule
  makespan and throughput
Least Flexible Job first (LFJ) rule
  makespan and throughput
Shortest Queue at the Next Operation (SQNO) rule
  machine idleness

## Slide 46: Single Machine Example

## Slide 47: Rules using Local Information
Example: Single machine case

## Slide 48: Pros and Cons of Dispatching Rules
• Advantages
– Simple to implement
– Can easily handle changing requirements by
updating priorities
• Disadvantages
– When task is popped, it is assigned to first
available resource
– If none available, it just waits, and nothing further
can be done
• Thus, susceptible to bottlenecks
– Doesn’t really set schedule times
• Can’t guarantee when things will get done
– No look-ahead, so no optimization
– No capability for JIT

## Slide 49: Dispatching Rules (cont.)
• However
– Much, if not most, real-world scheduling is done in this way
– Manual scheduling is often done in this
way

## Slide 50: Composite Dispatching Rules
Example:
  Single Machine with Weighted Total Tardiness
  No efficient algorithm (NP-Hard)
  Branch and bound can only solve very small problems (<30 jobs)
Are there any special cases we can solve?

## Slide 51: Case 1: Tight Deadlines
Assume dj=0
  Then
We know that WSPT is optimal for this problem!

## Slide 52: Case 2: Loose Deadlines
Theorem: If the deadlines are sufficiently spread out then the MS rule
is optimal (proof a bit harder)
Conclusion: The MS rule should be a good heuristic whenever deadlines are widely spread out

## Slide 53: Composite Rule
Two good heuristics
  Weighted Shorted Processing Time (WSPT )
    Optimal with due dates zero
  Minimum Slack (MS)
    Optimal when due dates are “spread out”
  Any real problem is somewhere in between
Combine the characteristics of these rules into one composite dispatching rule

## Slide 54: Apparent Tardiness Cost (ATC)
New ranking index
When machine becomes free:
  Compute index for all remaining jobs
  Select job with highest value
Scaling constant

## Slide 55: Special Cases
If K is very large:
  ATC reduces to WSPT
If K is very small and no overdue jobs:
  ATC reduces to MS
If K is very small and overdue jobs:
  ATC reduces to WSPT applied to overdue jobs

## Slide 56: Choosing K
Value of K determined empirically
Related to the due date tightness factor
and the due date range factor

## Slide 57
Machine Scheduling:
Sequencing Theory for a Single Machine
(单机排序理论)

## Slide 58: Sequencing theory for a single machine
The scheduling rule that minimizes the mean flow time (最小化平均流程时间) is Shortest Processing Time
  The following measures are equivalent: mean flow time, mean waiting time, and mean lateness for single machine
  SPT minimizes mean flow time, mean waiting time, and mean lateness for single-machine sequencing.
Earliest due date minimizes the maximum lateness (最小化最大延迟).
Moore’s algorithm (1968) minimizes the number of tardy jobs (最小化拖期任务数)
Lawler’s algorithm (1973) is a powerful technique for solving a variety of constrained scheduling problems

## Slide 59: WSPT
Theorem: Weighted Shortest Processing Time first - called the WSPT rule - is optimal for
Note: The SPT rule starts with the job that has the shortest processing time, moves on the job with the second shortest processing time, etc.
WSPT starts with job with largest

## Slide 60: Proof (by contradiction)
Suppose it is not true and schedule S, that is not WSPT, is optimal.
  Then there are two adjacent jobs, say job j followed by job k such that
Do a pairwise interchange to get schedule S’
j
k
k
j

## Slide 61: Proof (continued)
The weighted completion time of the two jobs under S is
The weighted completion time of the two jobs under S’ is
Now:
Contradicting that S is optimal.

## Slide 62: Moore’s algorithm
1.Sequence the jobs according to the earliest due date to obtain the initial solution. That is d[1]<=d[2]<=….<=d[n]
2.Find the first tardy job in the current sequence, say job [i]. If none exists go to step 4
3.Consider jobs [1][2]…[i]. Reject the job with the largest processing time. Return to step 2
4.Form an optimal sequence by taking the current sequence and appending to it the rejected jobs. The jobs appended to the current sequence may be scheduled in any order because they constitute the tardy jobs.
Minimize number of tardy jobs

## Slide 63: Example
Job | 1 | 2 | 3 | 4 | 5 | 6
Due date | 15 | 6 | 9 | 23 | 20 | 30
Processing time | 10 | 3 | 4 | 8 | 10 | 6
Minimize the number of tardy jobs for a single machine

## Slide 64: Solution
Job | 2 | 3 | 1 | 5 | 4 | 6
Due date | 6 | 9 | 15 | 20 | 23 | 30
Processing time | 3 | 4 | 10 | 10 | 8 | 6
Completion time | 3 | 7 | 17 | 27 | 35 | 41
Sequence the job according to the EDD rule

## Slide 65: Solution (cont.)
Job | 2 | 3 | 5 | 4 | 6
Due date | 6 | 9 | 20 | 23 | 30
Processing time | 3 | 4 | 10 | 8 | 6
Completion time | 3 | 7 | 17 | 25 | 31

## Slide 66: Solution (cont.)
Job | 2 | 3 | 4 | 6
Due date | 6 | 9 | 23 | 30
Processing time | 3 | 4 | 8 | 6
Completion time | 3 | 7 | 15 | 21
To minimize the number of tardy jobs, the optimal sequence is 234651 or 234615.
The minimum number of tardy jobs is exactly 2.

## Slide 67: Lawler’s algorithm (1973)
Objective function
  gi is any nondecreasing function of flow time Fi
Minimizing maximum lateness
Minimizing maximum tardiness

## Slide 68: Lawler’s algorithm
Lawler’s algorithm first schedules the job to be completed last, then the job to be completed next to last, and so on. At each stage one determines the set of jobs not required to precede any other.

## Slide 69: Exercise
Tony D’Amato runs a local body shop that does automotive painting and repairs. On a particular Monday morning he has 6 cars waiting for repair. Three (1,2,3) are from a car rental company and he has agreed to finish 3 cars in the order of the dates that they were promised. Cars 4,5,6 are from a retail dealer who has requested that car 4 be completed first because a customer is waiting for it.
The times required to repair each of the cars (in days) and the associated promised completion dates are
Determine how the repair of the cars should be scheduled through the shop in order to minimize the maximum tardiness.
Job | 1 | 2 | 3 | 4 | 5 | 6
Processing time | 2 | 3 | 4 | 3 | 2 | 1
Due date | 3 | 6 | 9 | 7 | 11 | 7

## Slide 70: Solution
First we find the job scheduled last (sixth)
Among the candidates for the last position are those jobs that are not predecessors of other jobs. These are 3, 5, and 6.
The total processing time of all jobs is 15.
As the objective is to minimize the maximum tardiness, we compare the tardiness of these three jobs and pick the one with the smallest value.
min{15-9, 15-11, 15-7}=4, corresponding to job 5
Hence job 5 is scheduled last (position 6)

## Slide 71: Solution (cont.)
Next we find the job scheduled fifth
The candidates are jobs 3 and 6 only.
Current total processing time = 15-2=13
Min{13-9, 13-7}=4, corresponding to job 3
Hence job 3 is scheduled in the fifth position

## Slide 72: Solution (cont.)
Find the job scheduled fourth
Because job 3 is no longer on the list, job 2 now becomes a candidate.
Current total processing time = 13-4=9
Min{9-6, 9-7}=2, corresponding to job 6
Hence job 6 is scheduled in the fourth position

## Slide 73: Solution (cont.)
Find the job scheduled third
Job 6 has been scheduled, so job 4 now becomes a candidate along with job 2
Current total processing time = 9-1=8
Min{8-6, 8-7}=1, corresponding to job 4
Hence job 4 is schedule in the third position

## Slide 74: Solution (cont.)
We would find the job scheduled second
However, we are left with only jobs 1 and 2, which, because of the precedence constraints, must be scheduled in the order 1-2
Hence, the optimal sequence to minimize the maximum tardiness is
1-2-4-6-3-5

## Slide 75: Solution (cont.)
The value of objective function
Job | Processing time | Completion time | Due date | Tardiness
1 | 2 | 2 | 3 | 0
2 | 3 | 5 | 6 | 0
4 | 3 | 8 | 7 | 1
6 | 1 | 9 | 7 | 2
3 | 4 | 13 | 9 | 4
5 | 2 | 15 | 11 | 4

## Slide 76: Sequencing theory for a single machine
The scheduling rule that minimizes the mean flow time is Shortest Processing Time
  The following measures are equivalent: mean flow time, mean waiting time, and mean lateness for single machine
  SPT minimizes mean flow time, mean waiting time, and mean lateness for single-machine sequencing.
Earliest due date minimizes the maximum lateness.
Moore’s algorithm (1968) minimizes the number of tardy jobs
Lawler’s algorithm (1973) is a powerful technique for solving a variety of constrained scheduling problems

## Slide 77: *Another important single machine model
Jobs | 1 | 2 | 3 | 4
pj | 4 | 2 | 6 | 5
rj | 0 | 1 | 3 | 5
dj | 8 | 12 | 11 | 10
It is strongly NP-hard.
It often appears as a subproblem in heuristics for flowshop and jobshop problem
Branch and bound procedure: bounds for nodes can be obtained by solving the following problem.
Example:
Preemptive EDD rule

## Slide 78
(•,•,•,•)
(1,•,•,•)
(2,•,•,•)
(3,•,•,•)
(1,2,•,•)
(1,3,•,•)
(4,•,•,•)
(1,3,4,2)
LB: Lower Bound
LB=5
LB=7
LB=6
Level 0
Level 1
Level 2
Level 3

## Slide 79: Machine Scheduling: Flow Shop Scheduling Problem with two Machines （双机流水作业问题）

## Slide 80: Flow Shop Scheduling Problem with two Machines
Given a set of jobs that must go through a sequence of
two machines, what sequence will yield the minimum
makespan? Mapespan is sequence dependent.
Johnson’s algorithm (Johnson 1954): 1. Sort the processing times of the jobs on the two machines in two lists. 2. Find the shortest time in either list and remove job from both lists. If time came from first list, place job in first available position. If time came from second list, place job in last available position in sequence. 3. Repeat until lists are exhausted.
The resulting sequence will minimize makespan.

## Slide 81: Johnson’s Algorithm Example
• Data:
• Iteration 1: min time is 4 (job 1 on M1); place this job first and remove from lists:
job | Time on M1 | Time on M2
1 2 3 | 4 7 6 | 9 10 5
List 1 | List 2
4 (1) 6 (3) 7 (2) | 5 (3) 9 (1) 10 (2)

## Slide 82: Johnson’s Algorithm Example (cont.)
• Iteration 2: min time is 5 (job 3 on M2); place this job last and remove from lists:
• Iteration 3: only job left is job 2; place in remaining position (middle).
• Final Sequence: 1-2-3
• Makespan: 28

## Slide 83: Gantt Chart for Johnson’s Algorithm Example
Short task on M1 to Short task on M2 to
“load up” quickly. “clear out” quickly.

## Slide 84: Extension to 3 Machines
Label the machine A, B, and C. The 3-machine problem can be reduced to a 2-machine problem if the following condition is satisfied:
If either one of these conditions be satisfied, the problem is reduced to a 2-machine problem in the following way:

## Slide 85: Example
Following jobs are processed in the sequence A-B-C
Job | Machine |  | 
 | A | B | C
1 | 4 | 5 | 8
2 | 9 | 6 | 10
3 | 8 | 2 | 6
4 | 6 | 3 | 7
5 | 5 | 4 | 11

## Slide 86: Solution
Job | A’ | B’
1 | 9 | 13
2 | 15 | 16
3 | 10 | 8
4 | 9 | 10
5 | 9 | 15
The optimal sequence is: 1-4-5-2-3

## Slide 87: Machine Scheduling: More general flow shop scheduling problem （多机流水作业问题）

## Slide 88: Slope Heuristic
Compute the slope index for each job
Sequence the jobs in decreasing order of the slope index
  The slope index is large if the processing time on the downstream machines are large relative to the processing times on the upstream machines
  The slope index is small if the processing time on the downstream machine are small in comparison with that on upstream machines

## Slide 89: Example
jobs | 1 | 2 | 3 | 4 | 5
P1j | 5 | 5 | 3 | 6 | 3
P2j | 4 | 4 | 2 | 4 | 4
P3j | 4 | 4 | 3 | 4 | 1
P4j | 3 | 6 | 3 | 2 | 5

## Slide 90: Solution
Suggested sequences: 2-5-3-1-4 or 5-2-3-1-4
Makespan=32

## Slide 91
8.3 异序作业调度 (Job Shop Scheduling)

## Slide 92: Job Shop Scheduling
Have m machines and n jobs
Each job visits some or all of the machines
Customer order of small batches
  Wafer fabrication in semiconductor industry
  Hospital
Very difficult to solve

## Slide 93: Job Shop Example
Constraints
  Job follows a specific route
  One job at a time on each machine
(1,1)
(2,3)
(3,1)
(4,3)
(1,2)
(1,3)
(2,1)
(2,2)
(4,2)
(3,3)
Machine 1
Machine 2
Machine 3
Machine 4
(i, j): i - 机器; j - 工件

## Slide 94: Graph Representation
Each job follows a specific route through the job shop ...
(1,1)
(2,1)
(3,1)
(1,2)
(2,2)
(4,2)
(2,3)
(1,3)
(4,3)
(3,3)
Sink
Source
(Conjunctive arcs/合取弧)

## Slide 95
Graph Representation
Machine constraints must also be satisfied ...
(Disjunctive arcs/析取弧)
(1,1)
(2,1)
(3,1)
(1,2)
(2,2)
(4,2)
(2,3)
(1,3)
(4,3)
(3,3)
Sink
Source

## Slide 96: Solving the Problem
Select one of each pair of disjunctive arcs
The longest path in this graph G(D) determines the makespan
(1,1)
(2,1)
(3,1)
(1,2)
(2,2)
(4,2)
(2,3)
(1,3)
(4,3)
(3,3)
Sink
Source

## Slide 97: Feasibility of the Schedule
Are all selections feasible?
(1,1)
(2,1)
(3,1)
(1,2)
(2,2)
(4,2)
(2,3)
(1,3)
(4,3)
(3,3)
Sink
Source

## Slide 98: Disjunctive Programming
Minimize
Subject to
工件j在机器k上的加工
开始时间
工件j在机器i上的加工持续时间

## Slide 99: Solution Methods
Exact solution
  Branch and Bound
  20 machines and 20 jobs
Dispatching rules (16+)
Shifting Bottleneck
Search heuristics
  Tabu, SA, GA, etc.

## Slide 100: Types of Schedules
A schedule is nondelay if no machine is idled when there is an operation available
A schedule is called active if no operation can be completed earlier by altering the sequence on machines and not delaying other operations
For “regular” objectives the optimal schedule is always active but not necessarily nondelay

## Slide 101: Nonactive Schedule
(3,2)
Machine 2
Machine 1
Machine 3
(1,1)
(2,3)
(2,2)
(2,1)
0 2 4 6 8
(2,1)

## Slide 102: Active Schedule, not Nondelay
(3,2)
Machine 2
Machine 1
Machine 3
(1,1)
(2,3)
(2,2)
(2,1)
0 2 4 6 8
Delay (Operation (2,1) does not fit)

## Slide 103: Nondelay schedule
(3,2)
Machine 2
Machine 1
Machine 3
(1,1)
(2,3)
(2,2)
(2,1)
0 2 4 6 8

## Slide 104
Job Shop Scheduling: The Shifting Bottleneck Heuristic
For makespan objective
(工期目标的移动瓶颈法)

## Slide 105: Shifting Bottleneck
Minimize makespan in a job shop
Let M denote the set of machines
Let M0  M be machines for which disjunctive arcs have been selected
Basic idea:
  Select a machine in M - M0 to be included in M0
  Sequence the operations on this machine

## Slide 106: Example

## Slide 107: Iteration 1
(1,1)
(2,1)
(3,1)
(2,2)
(1,2)
(3,2)
(1,3)
(2,3)
(4,3)
Sink
Source
(4,2)
0
10
8
4
8
3
5
6
4
7
3
0
0

## Slide 108: Selecting a Machine
Set up a nonpreemptive single machine maximum lateness
problem for Machine 1:
Optimum sequence is 1,2,3 with Lmax(1)=5
关键路径法得到最早
开始时间
关键路径法得到最晚
结束时间

## Slide 109
Selecting a Machine
Set up a nonpreemptive single machine maximum lateness
problem for Machine 2:
Optimum sequence is 2,3,1 with Lmax(2)=5

## Slide 110: Selecting a Machine
Similarly,
 Either Machine 1 or Machine 2 is the bottleneck

## Slide 111
Iteration 2
(1,1)
(2,1)
(3,1)
(2,2)
(1,2)
(3,2)
(1,3)
(2,3)
(4,3)
Sink
Source
(4,2)
0
10
8
4
8
3
5
6
4
7
3
0
0
10
3

## Slide 112
Selecting a Machine
Set up a nonpreemptive single machine maximum lateness
problem for Machine 2:
Optimum sequence is 2,1,3 with Lmax(2)=1

## Slide 113
Selecting a Machine
Similarly,
 Either Machine 2 or Machine 3 is the bottleneck

## Slide 114
Iteration 3
(1,1)
(2,1)
(3,1)
(2,2)
(1,2)
(3,2)
(1,3)
(2,3)
(4,3)
Sink
Source
(4,2)
0
10
8
4
8
3
5
6
4
7
3
0
0
10
3
8
8

## Slide 115: Discussion
Procedure continues until all the disjunctive arcs have been added
Extremely effective
  Fast
  Good solutions
‘Just a heuristic’
  No guarantee of optimum

## Slide 116: Discussion
Shifting bottleneck can be applied generally
Basic idea
  Solve problem “one variable at a time”
  Determine the “most important” variable
  Find the best value of that variable
  Move on to the “second most important” ….
  Here we treat each machine as a variable

## Slide 117: Exercise
Consider the following instance of the job shop problem with no recirculation and the makespan as objective
Jobs | m/c sequence | Processing time
1 | 1,2,3 | p11=9; p21=8; p31=4
2 | 1,2,4 | p12=5; p22=6; p42=3
3 | 3,1,2 | p33=10; p13=4; p23=9

## Slide 118
Job Shop Scheduling: Shifting Bottleneck for Total Weighted Tardiness Objective

## Slide 119: Total Weighted Tardiness
We now apply a shifted bottleneck procedure to a job shop with total weighted tardiness objective
  Need n sinks in disjunctive graph
  Machines scheduled one at a time
  Given current graph calculate completion time of each job
  Some n due dates for each operation
  Piecewise linear penalty function

## Slide 120: Cost Function for Operation (i,j)

## Slide 121: Machine Selection
Machine criticality
  Solve a single machine problem
  Piecewise linear cost function
  May have delayed precedence constraints
  Generalizes single-machine with n jobs, precedence constraints, and total weighted tardiness objective
  ATC rule

## Slide 122: Generalized ATC Rule
Earliest time machine can be used
Scaling constant
Ranks jobs
 good schedule

## Slide 123: Criticality of Machines
Criticality = subproblem objective function
  Simple
More effective ways, e.g.
  Add disjunctive arcs for each machine
  Calculate new completion times and

## Slide 124: Example
(1,1)
(2,1)
(3,1)
(3,2)
(1,2)
(3,3)
(2,3)
(1,3)
Sink
Source
(2,2)
5
5
10
4
4
5
6
5
3
7
0
0
Sink
Sink
w1=1; w2=2; w3=2

## Slide 125: Subproblem: Machine 1

## Slide 126
Subproblem: Machine 2

## Slide 127
Subproblem: Machine 3

## Slide 128: Subproblem Solutions
Solve using dispatching rule
  Use K=0.1
  Have t = 4,
For machine 1 this results in
Schedule
first

## Slide 129: Solution to Subproblems
Schedule
first

## Slide 130
First Iteration
(1,1)
(2,1)
(3,1)
(3,2)
(1,2)
(3,3)
(2,3)
(1,3)
Sink
Source
(2,2)
5
5
10
4
4
5
6
5
3
7
0
0
Sink
Sink
5
5

## Slide 131
Subproblem: Machine 2

## Slide 132
Subproblem: Machine 3

## Slide 133
Solution to Subproblems
Schedule
first

## Slide 134
Second Iteration
(1,1)
(2,1)
(3,1)
(3,2)
(1,2)
(3,3)
(2,3)
(1,3)
Sink
Source
(2,2)
5
5
10
4
4
5
6
5
3
7
0
0
Sink
Sink
5
5
3
10

## Slide 135
Subproblem: Machine 3

## Slide 136
Third Iteration
(1,1)
(2,1)
(3,1)
(3,2)
(1,2)
(3,3)
(2,3)
(1,3)
Sink
Source
(2,2)
5
5
10
4
4
5
6
5
3
7
0
0
Sink
Sink
5
5
3
10
5
4

## Slide 137: Final Schedule
0 5 10 15 20 25 30
3,3
3,2
2,3
1,1
1,2
2,1
2,2
3,1
1,3
Machine 1
Machine 2
Machine 3

## Slide 138: Performance
Objective function
Try finding a better schedule?
(optimal value = 18)

## Slide 139: 生产调度
小结