## Slide 1
Chapter 4 Local Area network

## Slide 2: LAN technologies
Data link layer so far:
  services, error detection/correction, multiple access
Next: LAN technologies
  LAN model
  addressing
  Ethernet
  hubs, switches
  802.11
  802.15

## Slide 3: Keypoints and Difficulties
Keypoints:
LAN model
Ethernet
Hubs, switches
Wireless LAN-IEEE 802.11
Difficulties:
The minimum frame length
The exponential Backoff algorithm
CSMA/CA

## Slide 4: LAN model
Data link
layer
Physical
layer
Network
layer
MAC sub layer
LLC sub layer
Logical Link Control
Media Access Control
Provide the connection environment to the upper level
Providing media access to the lower layer

## Slide 5: LAN model
Local area
network
Network
layer
Physical
layer
node 1
Network
layer
Physical
layer
Logic link
control
LLC
LLC
Media access
control
MAC
MAC
Data link
layer
node 2
The following LAN is invisible
for LLC sub layer
For the same LLC, several MAC options may be provided.

## Slide 6: LLC and MAC

## Slide 7: IEEE 802 working group
802.1A
802.1D Bridge
802.2 LLC
802.3
CSMA/CD
802.4
Token
Bus
802.6
DBDQ
802.8
FDDI
……
802.5
Token
ring
LLC
MAC
PHY

## Slide 8: LAN Addresses
32-bit IP address:
network-layer address
used to get datagram to destination network
LAN (or MAC or physical) address:
used to get datagram from one interface to another physically-connected interface (same network)
48 bit MAC address (for most LANs) burned in the adapter ROM

## Slide 9: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address
MAC flat address => portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  depends on network to which one attaches

## Slide 10: LAN Address
Each adapter on LAN has unique LAN address

## Slide 11: MAC Addresses
https://standards-oui.ieee.org/oui/oui.txt
MAC地址查询 - https://mac.bmcx.com/
What is the random MAC address technology?

## Slide 12: Ethernet
“dominant” LAN technology:
cheap $20 for 100Mbs!
first wildey used LAN technology
Simpler, cheaper than token LANs and ATM
Kept up with speed race: 10, 100, 1000 Mbps
Metcalfe’s Etheret
sketch

## Slide 13: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
star: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star

## Slide 14: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 15: 802.3 Ethernet standards: link & physical layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer

## Slide 16: Ethernet Frame Structure
Ethernet MAC frame
Physical
layer
MAC layer
10101010101010 10101010101010101011
Preamble field
Start of Frame Delimiter ; SFD
7 byte
1 byte
…
8 byte
inserting
IP layer
Destination
address
Source
address
type
data
FCS
6
6
2
4
byte
46 ~ 1500
IP datagrame
MAC frame

## Slide 17: Ethernet Frame Structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates

## Slide 18: Ethernet Frame Structure (more)
Addresses: 6 bytes, frame is received by all adapters on a LAN and dropped if address does not match
Type: 2 bytes, indicates the higher layer protocol, mostly IP but others may be supported such as Novell IPX and AppleTalk)
CRC: 4 bytes, checked at receiver, if error is detected, the frame is simply dropped

## Slide 19: Ethernet Frame Structure (more)
Data: 46~1500 bytes
Minimum frame length: 64 bytes, why? (contention period 2 is 51.2 s for IEEE 802.3, R=10Mbps)
Maximum frame length: 1518 bytes, why?

## Slide 20: Exercises-1
In a LAN using CSMA / CD protocol, the transmission medium is a complete cable, the transmission rate is 1Gbps, and the signal propagation rate in the cable is 200000 km / s. if the minimum data frame length is reduced by 800 bits, the distance between the farthest two stations needs to be at least
(1) increased by 160m (2) increased by 80m (3) reduced by 160m (4) reduced by 80m

## Slide 21: Ethernet: uses CSMA/CD
A: sense channel, if idle
  then {
  transmit and monitor the channel;
      If detect another transmission
      then {
      abort and send jam signal;
        update # collisions;
        delay as required by exponential backoff algorithm;
        goto A
        }
      else {done with the frame; set collisions to zero}
    }
  else {wait until ongoing transmission is over and goto A}

## Slide 22: Ethernet: uses CSMA/CD

## Slide 23: Ethernet’s CSMA/CD (more)
Jam Signal: make sure all other transmitters are aware of collision; 48 bits;
collision
A
B

t
B sending a packet
Channel
Occupation
time
Jamming signal

TB
TJ
for A, a conflict
is detected
for B, a conflict
is detected

## Slide 24: Ethernet’s CSMA/CD (more)
Exponential Backoff:
Goal: adapt retransmission attemtps to estimated current load
  heavy load: random wait will be longer
delay is K x 512 bit transmission times (contention period: 2)
first collision: choose K from {0,1};
after second collision: choose K from {0,1,2,3}…
after ten or more collisions, choose K from {0,1,2,3,4,…,1023}
K=min(n,i),n: # collisions,n≤j(attempt limit);i:back off limit
For Ethernet, i=10,j=16
Notes: 使等待的时间随重传次数增大，以减小发送碰撞的概率，有利于系统的稳定，但公平性不好

## Slide 25: Interconnecting LANs
Q: Why not just one big LAN?
Limited amount of supportable traffic: on single LAN, all stations must share bandwidth
limited length: 802.3 specifies maximum cable length
large “collision domain” (can collide with many stations)

## Slide 26: Hubs
Physical Layer devices: essentially repeaters operating at bit levels: repeat received bits on one interface to all other interfaces
Hubs can be arranged in a hierarchy (or multi-tier design), with backbone hub at its top

## Slide 27: Hubs (more)
Each connected LAN referred to as LAN segment
Hubs do not isolate collision domains: node may collide with any node residing at any segment in LAN
Hub Advantages:
  simple, inexpensive device
  Multi-tier provides graceful degradation: portions of the LAN continue to operate if one hub malfunctions
  extends maximum distance between node pairs (100m per Hub)

## Slide 28: Hub limitations
single collision domain results in no increase in max throughput
  multi-tier throughput same as single segment throughput
individual LAN restrictions pose limits on number of nodes in same collision domain and on total allowed geographical coverage
cannot connect different Ethernet types (e.g., 10BaseT and 100baseT)

## Slide 29: Ethernet switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 30: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 31: Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 32: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 33: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 34: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send on just one link

## Slide 35: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 36: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 37: Institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 38: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 39: VLANs: motivation
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering

## Slide 40: VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 41: Port-based VLAN
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 42: VLANS spanning multiple switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1

## Slide 43
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q VLAN frame format
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type

## Slide 44: Wireless communications
the challenges of wireless communications
wireless communication standards
IEEE 802.11
IEEE 802.15.4
5G?

## Slide 45: the challenges of Wireless communications
fading: path loss, multipath effect, shadow effect, Doppler effect
interference: from other wireless communications
hidden terminal problem
security
mobility

## Slide 46: Wireless communication technology
Transmission range
1 Gb/s
100 Mb/s
10 Mb/s
1 Mb/s
100 kb/s
10 kb/s
Data rate
PAN LAN MAN WAN
802.15.4
ZigBee
802.15.1
Blue-tooth
802.15.3
UWB
802.11g, a
802.11b
802.16
2G
Mobile communication
3G
Mobile communication
4G
Mobile communication
Wi-Fi
WiMAX

## Slide 47: IEEE Wireless Technology
Local wireless networks
WLAN 802.11
802.11a
802.11b
802.11i/e/f/n/s…
802.11g
WiFi
Personal wireless networks
WPAN 802.15
802.15.4
802.15.1
Bluetooth
ZigBee
WMAN 802.16 (Broadband Wireless Access)
WiBro, 802.20
+ Mobility
WiMAX
802.15.3
UWB
WiFi5

## Slide 48: infrastructure vs. ad-hoc networks
infrastructure network
ad-hoc network
AP
AP
AP
wired network
AP: Access Point

## Slide 49: IEEE standard 802.11
mobile terminal
access point
fixed
terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure
network
LLC
LLC

## Slide 50: IEEE 802.11 physical layer
WiFi 6
OFDMA
MU-MIMO
1024-QAM
Spatial Reuse & BBS Coloring
Notes: Spatial Reuse 空分复用
对于给定的调制方案，SNR越高，BER越低
对于给定的SNR，具有较高比特传输率的调制技术将具有较高的BER

## Slide 51: IEEE 802.11 protocol architecture

## Slide 52: 802.11 - MAC layer
Traffic services
  Asynchronous Data Service (mandatory)
    implemented using DCF (Distributed Coordination Function)
  Time-Bounded Service (optional)
    implemented using PCF (Point Coordination Function)
Access methods
  DCF CSMA/CA (mandatory)
    Distributed Wireless MAC
    collision avoidance via randomized „back-off“ mechanism
    minimum distance between consecutive packets
    ACK packet for acknowledgements (not for broadcasts)
  DCF w/ RTS/CTS (optional)
    avoids hidden terminal problem
  PCF (optional)
    access point polls terminals
    Contention free

## Slide 53: 802.11 MAC functions
MAC layer covers three functional areas:
  Reliable data delivery
    ACK-based scheme for reliability (receiver sends ACK after each successful transmission)
  Medium access control
    CSMA/CA; collision avoidance, not collision detection, Why? How?
  Security
    Wired Equivalent Privacy (WEP),WEP relies on a secret key being shared by end hosts and APs

## Slide 54: DCF CSMA/CA Illustrated

## Slide 55: 802.11 - MAC
Priorities
  defined through different inter frame spaces
  SIFS (Short Inter Frame Spacing) :
    10μs (802.11b/g), 16 μs (802.11a)
    High priority, for ACK, CTS, polling response
  PIFS (PCF IFS) :
    PIFS = SIFS + Slot time, which is 20 μs 802.11b, 9 μs 802.11a/g
    medium priority, for time-bounded service using PCF
  DIFS (DCF IFS):
    DIFS = PIFS + Slot time
    lowest priority, for asynchronous data service
t
medium busy
SIFS
PIFS
DIFS
DIFS
next frame
contention
direct access if medium is free  DIFS

## Slide 56: CSMA/CA access method
  station ready to send starts sensing the medium (Carrier Sense based on CCA, Clear Channel Assessment)
  if the medium is free for the duration of an Inter-Frame Space (IFS), the station can start sending (IFS depends on service type)
  if the medium is busy, the station has to wait for a free IFS, then the station must additionally wait a random back-off time (collision avoidance, multiple of slot-time)
    Slot time = 20 μs for 802.11b, 9 μs in 802.11a/g
    CW_min = 16 for 802.11a, 32 for 802.11b
    CW_max = 1024
t
medium busy
DIFS
DIFS
next frame
contention window
(randomized back-off mechanism)
slot time
Notes: 12

## Slide 57: CSMA/CA access method (Continued)
  If another station occupies the medium during the back-off time of the station, the back-off timer stops (fairness)
  When back-off timer reaches zero, start transmission
    If more than one nodes decrement to zero at the same time, a collision will occur.
  If a collision occurs (missing ACK), the corresponding nodes double the CW size and choose their back-off time from the increase CW
  After successful transmission, CW size is reset to its min value.

## Slide 58: A simplified example
frozen residual backoff time
frame
frame
frame
frame
frame
DIFS
DIFS
DIFS
DIFS
CW
CW
CW
CW
backoff
backoff
backoff
backoff
A
B
C
D
E
t
t
t
t
t
frozen
frozen
frozen
frozen
frozen

## Slide 59: LAN hidden terminal problem
A and C cannot hear each other and think B is idle, then, they both send data to B. A collision appears at the destination, B.
A transmission range
C transmission range
A
B
C
D

## Slide 60: LAN exposed terminal problem
B is sending data to A. At the same time, C hopes to communication with D. But C senses a signal in the medium and dare not send the data.
A
D
C
B
？
B transmission range
C transmission range

## Slide 61: RTS/CTS
Sending unicast packets
  station can send RTS with reservation parameter after waiting for DIFS (reservation determines amount of time the data packet needs the medium)
  acknowledgement via CTS after SIFS by receiver (if ready to receive)
  other stations store medium reservations distributed via RTS and CTS
  Two (potentially different) NAV groups
t
SIFS
DIFS
data
ACK
defer access
other
stations
receiver
sender
data
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)

## Slide 62: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 63: RTS/CTS (Continued)
Avoid hidden terminal problems
Also, reduce bandwidth waste by collisions
  Data frame can be as large as 2300bytes
  RTS = 20bytes, CTS = 14bytes
  The bigger is the data frame, the more advantageous
  Price : extended delay and more resource consumption!
RTS threshold
  Enable RTS/CTS for frames which are bigger than RTS threshold
  Each node’s decision

## Slide 64: CSMA/CA access method
Notes: 12
如何降低冲突的概率：
1）增加不同优先级的帧间间隔时间，信道空闲时间必须大于IFS才能发送，保证高优先级帧优先发送而不和低优先级帧冲突；
2）信号由忙变为空闲且经过DIFS后，还要退避一段随机时间才能使用信道，以减少冲突可能性
3）使用RTS/CTS信道预约和虚拟载波监听机制（通过NAV：Network allocation vector网络分配向量），尽可能较少由于隐藏终端带来的冲突问题

## Slide 65: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 66
Internet
router
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing

## Slide 67
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for RDT)
frame type
(RTS, CTS, ACK, data)
802.11 frame: more

## Slide 68: 802.11 – MAC frame format
Type/subtype
  control frames(01), management frames(00), data frames(10)
  E.g., data frame: type=10,subtype=0000 beacon: type=00,subtype=1000 RTS: type= 01,subtype=1011
Sequence numbers
  important against duplicated frames due to lost ACKs
Addresses
  receiver, transmitter (physical), BSS identifier, sender (logical)
Miscellaneous
  duration, checksum, frame control, data
2
2
6
6
6
6
2
4
0-2312
bytes
Frame
Control
Duration/
ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
Data
CRC
Protocol
version
Type
Subtype
To
DS
More
Frag
Retry
Power
Mgmt
More
Data
WEP
2
2
4
1
From
DS
1
Order
bits
1
1
1
1
1
1

## Slide 69: MAC address format
DS: Distribution System
AP: Access Point
DA: Destination Address
SA: Source Address
BSSID: Basic Service Set Identifier – MAC address of AP, cf: (E)SSID
RA: Receiver Address (AP)
TA: Transmitter Address (AP)

## Slide 70: Special Frames: ACK, RTS, CTS
Acknowledgement
Request To Send
Clear To Send
Frame
Control
Duration
Receiver
Address
Transmitter
Address
CRC
2
2
6
6
4
bytes
Frame
Control
Duration
Receiver
Address
CRC
2
2
6
4
bytes
Frame
Control
Duration
Receiver
Address
CRC
2
2
6
4
bytes
ACK
RTS
CTS

## Slide 71: Wireless communication technology
Transmission range
1 Gb/s
100 Mb/s
10 Mb/s
1 Mb/s
100 kb/s
10 kb/s
Data rate
PAN LAN MAN WAN
802.15.4
ZigBee
802.15.1
Bluetooth
802.15.3
UWB
802.11g, a
802.11b
802.16
2G
Mobile communication
3G
Mobile communication
4G
Mobile communication
Wi-Fi
WiMAX

## Slide 72: Wireless standards

## Slide 73: IEEE 802.15.4 and ZigBee
IEEE 802.15.4 Working Group
Defining lower layers of protocol stack: MAC and PHY
ZigBee Alliance
Defining upper layers of protocol stack from network to application

## Slide 74: ZigBee overview
ZigBee was created to address the market need for a cost-effective, standards based wireless networking solution that supports low data-rates, low-power consumption, security, and reliability.
ZigBee is the only standards-based technology that addresses the unique needs of most remote monitoring and control and sensory network applications.
The initial markets for the ZigBee Alliance include Home Automation, Building Automation and Industrial Automation.

## Slide 75: How to achieve low power consumption?
The duty cycle of battery is designed to be very low, resulting in very low average power consumption.
Once associated with a network, a ZigBee node can wake up and communicate with other devices and return to sleep.
Short range operation.
Simple but flexible protocol.

## Slide 76: Interference and Coexistence in the 2.4GHz Band

## Slide 77: Chapter 4:Local area network Summary
various link layer technologies
  LAN model
  Ethernet
  hubs, switches
  VLAN
  IEEE 802.11
  IEEE 802.15