## Slide 1: Chapter 5: Network Layer
Chapter goals:
understand principles behind network layer services:
  Network layer service models
  Forwarding versus routing
  how a router works
  routing (path selection)
  dealing with scale
instantiation and implementation in the Internet

## Slide 2: Chapter 5: Network Layer
5.1 Introduction
5.2 Virtual circuit and datagram networks
5.3 What’s inside a router?
5.4 Routing algorithms:
  Dijkstra’s algorithm
  Broadcast routing
  Link state
  Distance vector
  Hierarchical routing
5.5 Routing in the Internet
5.6 IP: Internet protocol
  IPv4 Datagram format
  IPv4 addressing
  IP fragment
  NAT
  ARP
  ICMP
  IPv6

## Slide 3: Keypoints and Difficulties
Keypoints:
Link state routing algorithm
Distance vector routing algorithm
IPv4
IPv6
Difficulties:
Virtual circuit and datagram networks
Subnet and Subnet Division
IP fragment

## Slide 4: Network layer
Transport packet from sending to receiving hosts
Network layer protocols in every host, router
Router examines header fields in all IP datagram passing through it
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 5: Two key Network-layer functions
Routing: determine route taken by packets from source to dest.
Routing algorithms
Forwarding: move packets from router’s input to appropriate router output
Analogy:
Routing: process of planning trip from source to dest.
Forwarding: process of getting through single interchange
Connection setup: some network architectures require router connection setup along path before data flows.

## Slide 6: Interplay between routing and forwarding

## Slide 7: Network service model
Q: What service model for “channel” transporting packets from sender to receiver?
guaranteed bandwidth?
preservation of inter-packet timing (no jitter)?
loss-free delivery?
in-order delivery?
congestion feedback to sender?
?
?
?
virtual circuit
or
datagram?
The most important
abstraction provided
by network layer:
service abstraction

## Slide 8: Network layer connection and connection-less service
Datagram network provides network-layer connectionless service
VC network provides network-layer connection service
Analogous to the transport-layer services,but:
Service: host-to-host
No choice: network provides one to the other
Implementation: in network core

## Slide 9: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 10: Chapter 5: Network Layer
5.1 Introduction
5.2 Virtual circuit and datagram networks
5.3 What’s inside a router?
5.4 Routing algorithms:
  Dijkstra’s algorithm
  Broadcast routing
  Link state
  Distance vector
  Hierarchical routing
5.5 Routing in the Internet
5.6 IP: Internet protocol
  IPv4 Datagram format
  IPv4 addressing
  IP fragment
  NAT
  ARP
  ICMP
  IPv6

## Slide 11: Virtual circuits: signaling protocols
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 12: Virtual circuits
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host OD)
every router on source-dest path s maintain “state” for each passing connection
  transport-layer connection only involved two end systems
link, router resources (bandwidth, buffers) may be allocated to VC
  to get circuit-like perf.
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path

## Slide 13: VC Implementation
A VC consists of:
1. Path from source to destination
2. VC numbers, one number for each link along path
3. Entries in forwarding tables in routers along path
Packet belonging to VC carries VC number(rather than dest. address)
VC number can be changed on each link
New VC number comes from forwarding table

## Slide 15: Datagram networks: the Internet model
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets typically routed using destination host ID
  packets between same source-dest pair may take different paths
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 17: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
Link interface
0
1
2
3
Notes: 华科 vs 华科AIA

## Slide 18: Datagram or VC network: why?
Internet
data exchange among computers
  “elastic” service, no strict timing req.
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
many link types
  different characteristics
  uniform service difficult
ATM
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 19: Chapter 5: Network Layer
5.1 Introduction
5.2 Virtual circuit and datagram networks
5.3 What’s inside a router?
5.4 Routing algorithms:
  Dijkstra’s algorithm
  Broadcast routing
  Link state
  Distance vector
  Hierarchical routing
5.5 Routing in the Internet
5.6 IP: Internet protocol
  IPv4 Datagram format
  IPv4 addressing
  IP fragment
  NAT
  ARP
  ICMP
  IPv6

## Slide 20: Router Architecture Overview
Two key router functions:
run routing algorithms/protocol (RIP, OSPF, BGP)
switching datagrams from incoming to outgoing link

## Slide 21: Input Port Functions
Decentralized switching:
given datagram dest., lookup output port using routing table in input port memory
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet

## Slide 22: Input Port Queuing
Fabric slower that input ports combined -> queueing may occur at input queues
queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 23: Three types of switching fabrics

## Slide 24: Switching Via Memory
First generation routers:
packet copied by system’s (single) CPU
speed limited by memory bandwidth (2 bus crossings per datagram)
Modern routers:
input port processor performs lookup, copy into memory
Cisco Catalyst 8500
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 25: Switching Via Bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers

## Slide 26: Switching Via An Interconnection Network
overcome bus bandwidth limitations
Banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
Advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 27: Output Ports
Buffering required when datagrams arrive from fabric faster than the transmission rate
Scheduling discipline chooses among queued datagrams for transmission
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 28: Output port queueing
buffering when arrival rate via switch exceeeds ouput line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 29: Chapter 5: Network Layer
5.1 Introduction
5.2 Virtual circuit and datagram networks
5.3 What’s inside a router?
5.4 Routing algorithms:
  Dijkstra’s algorithm
  Broadcast routing
  Link state
  Distance vector
  Hierarchical routing
5.5 Routing in the Internet
5.6 IP: Internet protocol
  IPv4 Datagram format
  IPv4 addressing
  IP fragment
  NAT
  ARP
  ICMP
  IPv6

## Slide 30: Interplay between routing and forwarding

## Slide 31: Routing
Graph abstraction for routing algorithms:
graph nodes are routers
graph edges are physical links
  link cost: delay, $ cost, or congestion level
Goal: determine “good” path
(sequence of routers) thru
network from source to dest.
Routing protocol
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
“good” path:
  typically means minimum cost path
  other def’s possible

## Slide 32: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 33: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 34: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 35: Dijkstra’s algorithm
Net topology,link costs known to all nodes
Computes least cost paths from one node(source) to all other nodes
Iterative: after k iterations, know least cost path to k dest.’s
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. V
p(v): predecessor node along path from source to v
N’: set of nodes whose least cost path definitively known

## Slide 36: Dijkstra’s algorithm

## Slide 37
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra’s algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 38: Dijkstra’s algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 39: Dijkstra’s algorithm: example (2)
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:

## Slide 40: Broadcast routing
Flooding: Deliver packets from source to all other nodes
Broadcast storm
Controlled flooding:
Sequence-number-controlled flooding: add ID + broadcast sequence number into the broadcast packets
reverse path forwarding, RPF
Be able to avoid the broadcast storm

## Slide 41: Broadcast routing
Spanning-tree broadcast
Suppose you have a connected undirected graph
…then a spanning tree of the graph is a connected subgraph in which there are no cycles
Be able to avoid the transmission of redundancy broadcast packets

## Slide 42: Link state algorithm
Broadcast routing + Dijkstra’s algorithm
Having each node broadcast link-state packets to all other nodes → all nodes have an identical and complete view of the network.
Using Dijkstra’s algorithm compute the least-cost path from one node to all other nodes in the network
If a link cost changes, re-broadcast and re-compute

## Slide 43: Link state algorithm,discussion
Algorithm complexity: n nodes
Each iteration: need to check all nodes, w, not in N
N(n+1)/2 comparisons:O(n2)
More efficient implementations possible: O(nlogn)
Oscillations possible:
E.g., link cost = amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
A
D
C
B
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1

## Slide 44: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
Define
dx(y) := cost of least-cost path from x to y
Then
dx(y)=minv ｛c(x,v)+dv(y)｝
where min is taken over all neighbors v of x
For example:
Clearly, dv(z)=5, dw(z)=3, dx(z)=3
B-F equation says:
du(z)=min｛c(u,v)+dv(z), c(u,x)+dx(z),
c(u,w)+dw(z)｝
=min(2+5,1+3,5+3)=4

## Slide 45: Distdance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 46: Bellman-Ford Example

## Slide 47: Distdance vector algorithm
Basic idea:
Each node periodically sends its own distance vector estimate to neighbors
When a node x receives new DV estimate from neighbor, it updates its own DV using B-F equation
Dx(y) ← minv{c(x,v)+Dv(y)} for each node yє N
Under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 48: Distance vector algorithm
Iterative, asynchronous:
Each local iteration caused by:
Local link cost change
DV update message from neighbor
Distributed:
Each node notifies neighbors only when its DV change
Neighbors then notify their neighbors if necessary

## Slide 49
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 50
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 51: Distance vector: link cost changes
Link cost changes:
Node detects local link cost change
Updates routing info, recalculates distance vector
If DV changes, notigy neighbors
“good news travels fast, bad news travels slow”

## Slide 54: Count to infinity problem
Link cost changes:
good news travels fast
Bad news travels slow – “count to infinity” problem!
for example:
44 iterations before algorithm stabilizes

## Slide 57: How to solve count to infinity problem?
Poisoned reverse:
If Z routes through Y to get to X:
Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
Will this completely solve count to infinity problem?

## Slide 59: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
Convergence time varies
Speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
may have oscillations
DV:convergence time varies
may be routing loops
count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
Node can advertise incorrect link cost
Each node computes only its own table
DV:
DV node can advertise incorrect path cost
Each node’s table used by others
Error propagate thru network

## Slide 60: Hierarchical Routing
scale: with billions of destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 61: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
special routers in AS
run intra-AS routing protocol with all other routers in AS
also responsible for routing to destinations outside AS
  run inter-AS routing protocol with other gateway routers
gateway routers

## Slide 62: Intra-AS and Inter-AS routing
Gateways:
  perform inter-AS routing amongst themselves
  perform intra-AS routers with other routers in their AS
inter-AS, intra-AS routing in
gateway A.c
network layer
link layer
physical layer
a
b
b
a
a
C
A
B
d
A.a
A.c
C.b
B.a
c
b
c

## Slide 63: Intra-AS and Inter-AS routing
Host
h2
a
b
b
a
a
C
A
B
d
c
A.a
A.c
C.b
B.a
c
b
Host
h1
Intra-AS routing
within AS A
Inter-AS
routing
between
A and B
Intra-AS routing
within AS B
We’ll examine specific inter-AS and intra-AS Internet routing protocols shortly

## Slide 64: Routing in the Internet
The Global Internet consists of Autonomous Systems (AS) interconnected with each other:
  Stub AS: small corporation
  Multihomed AS: large corporation (no transit)
  Transit AS: provider
Two-level routing:
  Intra-AS: administrator is responsible for choice
  Inter-AS: unique standard

## Slide 65: Internet AS Hierarchy
Inter-AS border (exterior gateway) routers
Intra-AS interior (gateway) routers

## Slide 66: Chapter 5: Network Layer
5.1 Introduction
5.2 Virtual circuit and datagram networks
5.3 What’s inside a router?
5.4 Routing algorithms:
  Dijkstra’s algorithm
  Broadcast routing
  Link state
  Distance vector
  Hierarchical routing
5.5 Routing in the Internet
5.6 IP: Internet protocol
  IPv4 Datagram format
  IPv4 addressing
  IP fragment
  NAT
  ARP
  ICMP
  IPv6

## Slide 67: Intra-AS Routing
Also known as Interior Gateway Protocols (IGP)
Most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol
  (Cisco proprietary for decades, until 2016)

## Slide 68: RIP ( Routing Information Protocol)
Distance vector algorithm
Included in BSD-UNIX Distribution in 1982
Distance metric: # of hops (max = 15 hops)
  Can you guess why?
Distance vectors: exchanged every 30 sec via Response Message (also called advertisement)
Each advertisement: route to up to 25 destination nets

## Slide 69: RIP (Routing Information Protocol)
Destination Network Next Router Num. of hops to dest.
w A 2
y B 2
z B 7
x -- 1
…. …. ....
w
x
y
z
A
C
D
B
Routing table in D

## Slide 70: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly propagates to entire net
  poison reverse used to prevent ping-pong loops (infinite distance = 16 hops)

## Slide 71: RIP Table processing
RIP routing tables managed by application-level process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated

## Slide 72: RIP Table example (continued)
Router: giroflee.eurocom.fr
Three attached class C networks (LANs)
Router only knows routes to attached LANs
Default router used to “go up”
Route multicast address: 224.0.0.0
Loopback interface (for debugging)
Destination Gateway Flags Ref Use Interface
-------------------- -------------------- ----- ----- ------ ---------
127.0.0.1 127.0.0.1 UH 0 26492 lo0
192.168.2. 192.168.2.5 U 2 13 fa0
193.55.114. 193.55.114.6 U 3 58503 le0
192.168.3. 192.168.3.5 U 2 25 qaa0
224.0.0.0 193.55.114.6 U 3 0 le0
default 193.55.114.129 UG 0 143454

## Slide 73: OSPF (Open Shortest Path First)
“open”: publicly available
Uses Link -State algorithm
  LS packet dissemination
  Topology map at each node
  Route computation using Dijkstra’s algorithm
OSPF advertisements are disseminated to entire AS (via flooding)
Link state advertisements are periodically updated
OSPF advertisements in OSPF messages are carried directly by IP

## Slide 74: OSPF “advanced” features (not in RIP)
Security: all OSPF messages authenticated (to prevent malicious intrusion); TCP connections used
Multiple same-cost paths allowed (only one path in RIP)
For each link, multiple cost metrics for different TOS (eg, satellite link cost set “low” for best effort; high for real time)
Integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
Hierarchical OSPF in large domains.

## Slide 75: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 76: Hierarchical OSPF
Two-level hierarchy: local area, backbone.
  Link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
Area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
Backbone routers: run OSPF routing limited to backbone.
Boundary routers: connect to other ASs.

## Slide 77: IGRP (Interior Gateway Routing Protocol)
CISCO proprietary; successor of RIP (mid 80s)
Distance Vector, like RIP
several cost metrics (delay, bandwidth, reliability, load etc)
uses TCP to exchange routing updates
Loop-free routing via Distributed Updating Alg. (DUAL) based on diffused computation

## Slide 78: Inter-AS routing

## Slide 79: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
Path Vector protocol:
  similar to Distance Vector protocol
  each Border Gateway broadcast to neighbors (peers) entire path (I.e, sequence of ASs) to destination
  E.g., Gateway X may send its path to dest. Z:
Path (X,Z) = X,Y1,Y2,Y3,…,Z

## Slide 80: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto standard
BGP provides each AS a means to:
  Obtain subnet reachability information from neighboring ASs.
  Propagate reachability information to all AS-internal routers.
  Determine good routes to subnets based on reachability information and policy.
  Allows subnet to advertise its existence to the rest of Internet: “I am here”

## Slide 81: BGP route selection
Router may learn about more than 1 route to some prefix. Router must select route
Elimination rules:
  Local preference value attribute: policy decision
  Shortest AS-PATH
  Closest NEXT-HOP router: hot potato routing
  Additional criteria

## Slide 82: Internet inter-AS routing: BGP
Suppose: gateway X send its path to peer gateway W
W may or may not select path offered by X
  cost, policy (don’t route via competitors AS), loop prevention reasons.
If W selects path advertised by X, then:
Path (W,Z) = w, Path (X,Z)
Note: X can control incoming traffic by controling it route advertisements to peers:
  e.g., don’t want to route traffic to Z -> don’t advertise any routes to Z

## Slide 83: Internet inter-AS routing: BGP
BGP messages exchanged using TCP.
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 84: BGP Routing Policy
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
X does not want to route from B via X to C
…so X will not advertise to B a route to C

## Slide 85: BGP Routing Policy
A advertises to B the path AW
B advertises to X the path BAW
Should B advertise to C the path BAW?
No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
B wants to force C to route to W via A
B wants to route only to/from its customers!

## Slide 86: Why different Intra- and Inter-AS routing ?
Policy:
Inter-AS: admin wants control over how its traffic routed, who routes through its net.
Intra-AS: single admin, so no policy decisions needed
Scale:
hierarchical routing saves table size, reduced update traffic
Performance:
Intra-AS: can focus on performance
Inter-AS: policy may dominate over performance

## Slide 87: Exercises-1
The protocols for directly encapsulating RIP、 OSPF and BGP messages are
A. TCP、UDP、IP
B. TCP、IP、UDP
C. UDP、TCP、IP
D. UDP、IP、TCP
Notes: D

## Slide 88: *Network layer: data plane, control plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
1
2
3
0111
values in arriving
packet header

## Slide 89
*Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 90
data
plane
control
plane
*Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 91
*Generalized Forwarding and SDN
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each router contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions

## Slide 92: *OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Notes: Now I’ll describe the API that tries to meet these goals.
92

## Slide 93: *OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies different kinds of devices

## Slide 94: *OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 95: Homework
P455:R4,R5
P457:P3,P5
P458:P11
P396:P14

## Slide 96: Chapter 5: Network Layer
5.1 Introduction
5.2 Virtual circuit and datagram networks
5.3 What’s inside a router?
5.4 Routing algorithms:
  Dijkstra’s algorithm
  Broadcast routing
  Link state
  Distance vector
  Hierarchical routing
5.5 Routing in the Internet
5.6 IP: Internet protocol
  IPv4 Datagram format
  IPv4 addressing
  IP fragment
  NAT
  ARP
  ICMP
  IPv6

## Slide 97: The Internet Network layer
routing
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 98: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 99: Upper-layer protocol field
Transport layer
Network layer
header
TCP:6
UDP:17
ICMP:1
IGMP
OSPF:89
data
IP datagram
The field indicates which upper-layer protocol the data should be passed to.

## Slide 100: Header checksum
sender
receiver
16 bit
word 1
16 bit
word 2
all bits = 0
checksum
16 bit
word n
16 bit
complement arithmetic sum
…
…
NOT operator
Header of IP
IP datagram
16 bit
checksum
16 bit
word 1
16 bit
word 2
16 bit
checksum
16 bit
word n
16 bit
complement arithmetic sum
16 bit
result
…
…
NOT operator
data
If sum=0000000000000000,
no errors
Data field does not join in
the calculation of checksum

## Slide 101: Internet checksum: example
example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 102: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 103: IP Fragmentation
offset = 0/8 = 0
offset = 0/8
= 0
offset = 1400/8 = 175
offset = 2800/8 = 350
1400
2800
3799
2799
1399
3799
One large
datagram
fragment 1
header
3800 bytes Data
header 1
Header 2
Header 3
byte 0
fragment 2
fragment 3
1400
2800
byte 0

## Slide 104: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 105: IP datagram
Now assume a IP datagram is captured. The first 20 bytes are as follows:
0x45 0x00 0x00 0x3C 0x1A 0x37 0x00 0x00 0x80 0x01 0x6E 0x31 0xC0 0xA8 0x01 0xD4 0xD3 0x9B 0x1C 0x41
Please try to analyze the value and meaning of each field in the IP datagram header.

## Slide 106: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 107: IP addressing: introduction
Q: how are interfaces actually connected?
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)

## Slide 108: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 109: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 110: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 111: IP Addresses
0
network
host
10
network
host
110
network
host
1110
multicast address
A
B
C
D
class
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
32 bits
given notion of “network”, let’s re-examine IP addresses:
“class-full” addressing:

## Slide 112
网络号 | 主机号 | 地址类型 | 用途
全0 | 全0 | 本机 | 启动时使用
网络ID | 全0 | 网络 | 标识一个网络
网络ID | 全1 | 直接广播 | 在指定网上广播
全1 | 全1 | 有限广播 | 在本地网上广播
127 | 任意 | 回送 | 环回测试（127.0.0.1）

## Slide 113: IP addressing
Dotted-decimal notation:193.32.216.9
classful addressing:
  inefficient use of address space, address space exhaustion
  e.g., class B net allocated enough addresses for 65K hosts, even if only 2K hosts in that network
Subnetting and subnet mask
11001000 00010111 00010000 01000000
network
part
host
part
200.23.16.64/27
subnet
part

## Slide 114: A class B network without subnet: 145.13.0.0
…
…
…
145.13.3.10
145.13.3.11
145.13.3.101
145.13.7.34
145.13.7.35
145.13.7.56
145.13.21.23
145.13.21.9
145.13.21.8
All packets to 145.13.0.0 can reach this router
My network ID
is 145.13.0.0
R1
R3
R2
network
145.13.0.0

## Slide 115: A network for others, the class B with 3 subnet
…
…
…
145.13.3.10
145.13.3.11
145.13.3.101
145.13.7.34
145.13.7.35
145.13.7.56
145.13.21.23
145.13.21.9
145.13.21.8
All packets to 145.13.0.0 can reach this router
My network ID
is 145.13.0.0
R1
R3
R2
network
145.13.0.0

## Slide 116: Subnet mask
Network ID
Host ID
Two level
IP address
网络号
Three level
IP address
主机号
Network ID
Host ID
Subnet ID
子网号
Subnet mask
Network ID
of the subnet
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
0 0 0 0 0 0 0 0
Network ID
Subnet ID
0
AND operation

## Slide 117: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  Two level address: only two parts
  network portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in network portion of address
  Network portion is often called prefix
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23

## Slide 118: CIDR example
Internet
206.0.68.0/22
206.0.64.0/18
ISP
university X
School 1
School 2
Scholl 3
School 4
206.0.71.128/26
206.0.71.192/26
206.0.68.0/25
206.0.68.128/25
206.0.69.0/25
206.0.69.128/25
206.0.70.0/26
206.0.70.64/26
206.0.70.128/26
206.0.70.192/26
206.0.70.0/24
206.0.71.0/25
206.0.71.0/26
206.0.71.64/26
206.0.71.128/25
206.0.68.0/23
organizatio address block binary number
ISP 206.0.64.0/18 11001110.00000000.01* 16384
Uni. X 206.0.68.0/22 11001110.00000000.010001* 1024
sch. 1 206.0.68.0/23 11001110.00000000.0100010* 512
Sch. 2 206.0.70.0/24 11001110.00000000.01000110.* 256
Sch.3 206.0.71.0/25 11001110.00000000.01000111.0* 128
Sch. 4 206.0.71.128/25 11001110.00000000.01000111.1* 128

## Slide 119: IP addresses: how to get one?
Hosts (host portion):
hard-coded by system admin in a file
DHCP: Dynamic Host Configuration Protocol: dynamically get address: “plug-and-play”
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 120: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 121: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 122: IP addresses: how to get one?
Network (network portion):
get allocated portion of ISP’s address space:
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 123: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing
information:

## Slide 124: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 125: IP addressing: the last word...
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 126: Exercise-2
1. In subnet 192.168.4.0/30, the maximum number of hosts that can accept IP packets with destination address 192.168.4.3 is
A.0 B.1 C.2 D.4
2. There are four routing table entries with the same forwarding interface in a routing table, and their destination network addresses are 35.230.32.0/21, 35.230.40.0/21, 35.230.48.0/21 and 35.230.56.0/21 respectively. After aggregating the four routes, the destination network address is
A.35.230.0.0/19 B. 35.230.0.0/20
C. 35.230.32.0/19 D. 35.230.32.0/20
Notes: 1.C 2. C

## Slide 127: Exercises-3
Assuming that the applied IP address block is 218.75.230.0/24, please assign IP addresses to the devices in the figure below using fixed length and variable length subnet masks respectively.

## Slide 128: Exercises-3
Assuming that the applied IP address block is 218.75.230.0/24, please assign IP addresses to the devices in the figure below using fixed length and variable length subnet masks respectively.

## Slide 129: Exercises-3
Assuming that the applied IP address block is 218.75.230.0/24, please assign IP addresses to the devices in the figure below using fixed length and variable length subnet masks respectively.

## Slide 130: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 131: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned
Implementation: NAT router must:
Outgoing datagrams: replace (source IP address, port #) to (NAT IP address, new port #)
Remember (in NAT translation table) every translation pair
Incoming datagrams: replace (NAT IP address, new port #) with correspongding (source IP address, port #) stored in NAT table

## Slide 132: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 133: NAT: Network Address Translation
Outside node cannot initiate the communication
Reserved addresses:
10.0.0.0 – 10.255.255.255
172.16.0.0 – 172.31.255.255
192.168.0.0 – 192.168.255.255

## Slide 134: LAN addresses and ARP
32-bit IP address:
network-layer address
used to get datagram to destination network (recall IP network definition)
LAN (or MAC or physical) address:
used to get datagram from one interface to another physically-connected interface (same network)
48 bit MAC address (for most LANs) burned in the adapter ROM
e.g.: 1A-2F-BB-76-09-AD

## Slide 135: ARP: Address Resolution Protocol
Each IP node (Host, Router) on LAN has ARP module, table
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
< ………………………….. >
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
MAC address of B
given B’s IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 136: ARP protocol：same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator
Notes: ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 137: Routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 138: Routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 139: Routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 140: Routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 141: Routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 142: Routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 143: Exercises-4
Figure 1 shows the network topology, and Figure 2 shows the hex-content of the first 80 bytes of an Ethernet frame of the host for a Web request.
(1) What is the IP address of the Web server? What is the MAC address of the default gateway of this host?
(2) When the IP packet encapsulated in this frame is forwarded through router R, which fields in the IP packet need to be modified？
Fig. 1
Fig. 2
Notes: (1)40 aa 62 20,64.170.98.32; 00-21-27-21-51-ee
(2) TTL字段，首部校验和重新计算，总长字段若大于MTU，则总长字段、标志字段、片偏移字段都需要修改

## Slide 144: ICMP: Internet Control Message Protocol
used by hosts, routers, gateways to communication network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 145: ICMP:brief summary
ICMP is the control sibling of IP
ICMP is used by IP and uses IP as network layer protocol
ICMP is used for ping, traceroute, and path MTU discovery
Ping: uses ICMP Echo request/reply messages
Path MTU discovery
Send a large IP datagram with”No fragment” bit set
Reduce size until success (No ICMP message received)

## Slide 146: ping

## Slide 147: traceroute

## Slide 148: Traceroute and ICMP
Source sends series of UDP segments to dest.
First has TTL=1
Second has TTL=2, etc.
Unlikely port number
When nth datagram arrives to nth router:
Router discards datagram
And sends to source an ICMP message (type 11, code 0)
Message includes name of router & IP address
When ICMP message arrives, source calculates RTT
Traceroute does this 3 times
Stopping criterion
UDP segment eventually arrives at destination host
Destination returns ICMP “host unreachable” packet (type 3, code 3)
When source gets this ICMP, stops

## Slide 149: IPv6
Initial motivation: 32-bit address space completely allocated by 2008.
Additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
  new “anycast” address: route to “best” of several replicated servers
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 150: IPv6 Header (Cont)
Priority: identify priority among datagrams in flow
Flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
Next header: identify upper layer protocol for data

## Slide 151: Next header
Effective payload
Effective payload
Basic header
Next header
= TCP/UDP
Basic header
Next header
= routing
selection
Routing header
Next header
= fragment
Fragment header
Next header
= TCP/UDP
TCP/UDP header
And data
(TCP/UDP segment）
TCP/UDP header
and data
(TCP/UDP segment）
Without extension header
With extension header

## Slide 152: Other Changes from IPv4
Checksum: removed entirely to reduce processing time at each hop
Options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 153: IPv6 address
Three types: unicast, multicast, anycast
Colon hexadecimal notation:
68E6:8C64:FFFF:FFFF:0:1180:960A:FFFF
Zero compression:
FF05:0:0:0:0:0:0:B3 == FF05::B3 ;
0:0:0:0:0:0:128.10.2.1 == ::128.10.2.1
12AB:0000:0000:CD30:0000:0000:0000:0000/60
== 12AB::CD30:0:0:0:0/60
== 12AB:0:0:CD30::/60

## Slide 154: Unicast address
First level
Third level
Interface ID
（64 bit）
Subnet
ID
（16 bit）
Second
level
Global routing prefix
（48 bit）
bit 0 48 64 127

## Slide 155: EUI-64
0xFFFE
low 24 bit
cccccc1gcccccccccccccccc 1111111111111110
ccccc c0gcccccccccccccccc
bit 0 8 24 47
bit 0 8 24 40 63
IEEE 802
address
interface
ID
low 24 bit
I/G bit
G/L bit
G/L = 1

## Slide 156
Example:
host MAC address: 00:0C:85:AB:50:01
insert FFFE： 00:0C:85:FF:FE:AB:50:01
set G/L bit: 02:0C:85:FF:FE:AB:50:01
host EUI-64 is: 020C:85FF:FEAB:5001
router advertise the 64bit network prefix
Host unicast address: prefix+EUI-64

## Slide 157: Transition From IPv4 To IPv6
Not all routers can be upgraded simultaneous
  no “flag days”
  How will the network operatewith mixed IPv4 and IPv6 routers?
Two proposed approaches:
  Dual Stack: some routers with dual stack (v6, v4) can “translate” between formats
  Tunneling: IPv6 carried as payload n IPv4 datagram among IPv4 routers

## Slide 158: Dual Stack Approach

## Slide 159: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 160: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4

## Slide 161: Summary
Virtual circuit and datagram networks
Routing algorithms:
  Dijkstra’s algorithm
  Broadcast routing
  Link state
  Distance vector (“count to infinity” problem)
Routing in the Internet (RIP, OSPF, BGP)
IP: Internet protocol
  IPv4 Datagram format
  IPv4 addressing
  IP fragment
  NAT
  ARP
  ICMP
  IPv6
  From IPv4 to IPv6

## Slide 162: Homework
P455:R4,R5
P457:P3,P5
P458:P11
P396:P14
P395:P8,P11,P12