## Slide 1: Chapter 6: Transport Layer
Our goals:
Understand principles behind transport layer services:
  Multiplexing/demultiplexing
  Reliable data transfer
  Flow control
  Congestion control
Learn about transport layer protocols in the Internet:
  UDP: connectionless transport
  TCP: connection-oriented transport
  TCP congestion control

## Slide 2: Keypoints and Difficulties
Keypoints:
Port numbers
TCP
Difficulties:
TCP connection management
TCP Reliable data transfer
TCP congestion control

## Slide 3: Chapter 6 Outline
6.1 Transport-layer services
6.2 Multiplexing and demultiplexing
6.3 Connectionless transport: UDP
6.4 Connection-oriented transport: TCP
  Segment structure
  Connection management
  Flow control
  Reliable data transfer
6.5 TCP congestion control

## Slide 4: Transport Services and Protocols
Provide logical communication between app processes running on different hosts
Transport protocols run in end systems
  Send side: breaks app messages into segments, passes to network layer
  Rcv side: reassembles segments into messages, passes to app layer
More than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 5: Transport vs. Network Layer
Network layer:
  Logical communication between hosts
Transport layer:
  Logical communication between processes
  Relies on, enhances, network layer services

## Slide 6: Transport vs. Network Layer
Household analogy:
12 kids sending letters to 12 kids
Processes = kids
App messages = letters in envelopes
Hosts = houses
Network-layer protocol = postal service
Transport protocol = Ann and Bill

## Slide 7: Internet Transport-Layer Protocols
Reliable, in-order delivery (TCP)
  Congestion control
  Flow control
  Connection setup
Unreliable, unordered delivery: UDP
  No-frills extension of “best-effort” IP
Services not available:
  Delay guarantees
  Bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport
Notes: Frills:装饰

## Slide 8: Chapter 6 Outline
6.1 Transport-layer services
6.2 Multiplexing and demultiplexing
6.3 Connectionless transport: UDP
6.4 Connection-oriented transport: TCP
  Segment structure
  Connection management
  Flow control
  Reliable data transfer
6.5 TCP congestion control

## Slide 9: Multiplexing/Demultiplexing
host 1
= process
= socket
1 host  1 or more processes
1 process  1 or more sockets
Transport layer interacts with socket
Demultiplexing at rcv host
Multiplexing at send host
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
Notes: Socket套接字：相当于从网络向进程传递数据和从进程向网络传递数据的门户，每个套接字都有唯一的标识符
对UDP而言，套接字相当于端口号，包含2元组（目的IP，目的端口号）
对TCP而言，因为其是面向连接的，TCP 使用“连接”(而不仅仅是“端口”)作为最基本的抽象，同时将 TCP 连接的端点称为套接字(socket) ，所以其套接字是4元组，包括源和目的IP地址
服务器主机同时支持多个并发的TCP套接字:每一个套接字都由其四元组来标识

## Slide 10: Multiplexing/Demultiplexing
Segment - unit of data exchanged between transport layer entities
  aka TPDU: transport protocol data unit
Demultiplexing at rcv host: : delivering received segments to
correct app layer processes
through socket
application
transport
network
M
P2
application
transport
network
receiver
H
t
H
n
segment
segment
M
application
transport
network
P1
M
M
M
P3
P4
segment
header
application-layer
data
Notes: Aka:亦称

## Slide 11: How Demultiplexing Works
Host receives IP datagrams
  Each datagram has source IP address, destination IP address
  Each datagram carries 1 transport-layer segment
  Each segment has source, destination port number (recall: well-known port numbers for specific applications)
Host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format
Notes:   端口的作用就是让应用层的各种应用进程都能将其数据通过端口向下交付给运输层，以及让运输层知道应当将其报文段中的数据向上通过端口交付给应用层相应的进程（或者线程）
  从这个意义上讲，端口是用来标志应用层的进程（或者线程）：端口用一个 16 bit 端口号进行标志
对UDP而言，套接字相当于端口号，包含2元组（目的IP，目的端口号）
对TCP而言，因为其是面向连接的，TCP 使用“连接”(而不仅仅是“端口”)作为最基本的抽象，同时将 TCP 连接的端点称为套接字(socket) ，所以其套接字是4元组，包括源IP,源端口号和目的IP地址、目的端口号
服务器主机同时支持多个并发的TCP套接字:每一个套接字都由其四元组来标识

## Slide 12: Well-known port number
The port number only has local meaning, and the same port number in different computers is not related.

## Slide 13: Multiplexing/Demultiplexing
Multiplexing/demultiplexing
  Based on sender, receiver port numbers, IP addresses
  <source IP #, dest. IP#, source port #, dest. port#>
gathering data from multiple sockets, enveloping data with header (later used for demultiplexing)
Multiplexing at send host:

## Slide 14: Multiplexing/Demultiplexing: examples
Host A
Server B
source port: x
dest. port: 23
source port: 23
dest. port: x
port use: simple telnet app
source IP: C
dest. IP: B
source port: y
dest. port: 80
source IP: C
dest. IP: B
source port: x
dest. port: 80
Web Server B
port use: web server
Web client Host C
Web client Host A
source IP: A
dest. IP: B
source port: x
dest. port: 80

## Slide 15: Connectionless Demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(12534);
DatagramSocket mySocket2 = new DatagramSocket(12535);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  Checks destination port number in segment
  Directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 16: Connectionless Demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
P2
client
IP: A
Client
IP:B
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”

## Slide 17: Connection-Oriented Demux
TCP socket identified by 4-tuple:
  Source IP address
  Source port number
  Dest IP address
  Dest port number
Recv host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  Each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  Non-persistent HTTP will have different socket for each request

## Slide 18: Connection-Oriented Demux (cont.)
P4
server
IP: C
P5
P6
Client
IP:B
P2
P3
P1
client
IP: A
SP: 9157
DP: 80
S-IP: A
D-IP: C
SP: 9157
DP: 80
D-IP: C
S-IP: B
SP: 5775
DP: 80
D-IP: C
S-IP: B

## Slide 19: Connection-Oriented Demux: Threaded Web Server
Client
IP:B
P2
P3
server
IP: C
P4
P1
client
IP: A
SP: 9157
DP: 80
S-IP: A
D-IP: C
SP: 9157
DP: 80
D-IP: C
S-IP: B
SP: 5775
DP: 80
D-IP: C
S-IP: B

## Slide 20: Chapter 6 Outline
6.1 Transport-layer services
6.2 Multiplexing and demultiplexing
6.3 Connectionless transport: UDP
6.4 Connection-oriented transport: TCP
  Segment structure
  Connection management
  Flow control
  Reliable data transfer
6.5 TCP congestion control

## Slide 21: UDP: User Datagram Protocol [RFC 768]
“No frills,” “bare bones” Internet transport protocol
“Best effort” service, UDP segments may be:
  Lost
  Delivered out of order to app
Connectionless:
  No handshaking between UDP sender, receiver
  Each UDP segment handled independently of others
Why is there a UDP?
No connection establishment (which can add delay)
Simple: no connection state at sender, receiver
Small segment header
No congestion control: UDP can blast away as fast as desired

## Slide 22: UDP: more
Often used for streaming multimedia apps
  Loss tolerant
  Rate sensitive
Other UDP uses
  DNS
  SNMP
Reliable transfer over UDP: add reliability at application layer
  Application-specific error recovery!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header
Notes: 检验和字段检验的范围包括首部和数据这两部分。在计算检验和时，要在 UDP 报文段的前面加上 12 字节的伪首部。

## Slide 23: Chapter 6 Outline
6.1 Transport-layer services
6.2 Multiplexing and demultiplexing
6.3 Connectionless transport: UDP
6.4 Connection-oriented transport: TCP
  Segment structure
  Connection management
  Flow control
  Reliable data transfer
6.5 TCP congestion control

## Slide 24: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
Connection-oriented:
  Handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
Full duplex data:
  Bi-directional data flow in same connection
  MSS: maximum segment size
End-to-End:
  One sender, one receiver
In-order byte steam:
  No “message boundaries”
Reliable :
  TCP congestion and flow control set window size
Notes:     TCP可靠传输：差错控制+流量控制+确认重传, 和数据链路层的可靠传输机制不一样的地方1）编号采用按字节编号，而非按报文段编号，引出seq和ACK的定义
什么是基于字节流？引出下一张PPT
全双工：背回技术
TCP 只规定了一种选项，即最大报文段长度 MSS (Maximum Segment Size)。MSS 告诉对方 TCP：“我的缓存所能接收的报文段的数据字段的最大长度是 MSS 个字节。

## Slide 25: TCP: byte stream
  Each byte is numbered in segment’s data
    E.g., Suppose that a process in Host A wants to send a stream of data (a file of 500,000 bytes) to a process in Host B over a TCP connection. MSS is 1,000 bytes, and the 1st byte is numbered 0.
    Seq # of the 1st segment: 0; Seq # of the 2nd segment: 1000;
    Seq # of the 3rd segment: ?

## Slide 26: TCP Seq. #’s and ACKs
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
Simple telnet scenario

## Slide 27: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)
Notes: 源端口和目的端口字段——各占 2 字节。端口是运输层与应用层的服务接口。运输层的复用和分用功能都要通过端口才能实现。
序号字段——占 4 字节。TCP 连接中传送的数据流中的每一个字节都编上一个序号。序号字段的值则指的是本报文段所发送的数据的第一个字节在整个报文字节流中的序号。
确认号字段——占 4 字节，是期望收到对方的下一个报文段的数据的第一个字节的序号。
首部长度——占 4 bit，它指示意32bit为单位的TCP首部长度。
保留字段——占 6 bit，保留为今后使用，但目前应置为 0。
紧急比特 URG —— 当 URG  1 时，表明紧急指针字段有效。它告诉系统此报文段中有紧急数据，应尽快传送。（一般不使用）
确认比特 ACK —— 只有当 ACK  1 时确认号字段才有效。当 ACK  0 时，确认号无效。
推送比特 PSH (PuSH) —— 接收 TCP 收到推送比特置 1 的报文段，就尽快地交付给接收应用进程，而不再等到整个缓存都填满了后再向上交付。
复位比特 RST (ReSeT) —— 当 RST  1 时，表明 TCP 连接中出现严重差错（如由于主机崩溃或其他原因），必须释放连接，然后再重新建立运输连接。
同步比特 SYN —— 同步比特 SYN 置为 1，就表示这是一个连接请求或连接接受报文。
终止比特 FIN (FINal) —— 用来释放一个连接。当FIN  1 时，表明此报文段的发送端的数据已发送完毕，并要求释放运输连接。
窗口字段 —— 占 2 字节。窗口字段用来控制对方发送的数据量，单位为字节。TCP 连接的一端根据设置的缓存空间大小确定自己的接收窗口大小，然后通知对方以确定对方的发送窗口的上限。
检验和 —— 占 2 字节。检验和字段检验的范围包括首部和数据这两部分。在计算检验和时，要在 TCP 报文段的前面加上 12 字节的伪首部。
紧急指针字段 —— 占 16 bit。紧急指针指出在本报文段中的紧急数据的最后一个字节的序号。
选项字段 —— 长度可变。TCP 只规定了一种选项，即最大报文段长度 MSS (Maximum Segment Size)。MSS 告诉对方 TCP：“我的缓存所能接收的报文段的数据字段的最大长度是 MSS 个字节。MSS 是 TCP 报文段中的数据字段的最大长度。
数据字段加上 TCP 首部才等于整个的 TCP 报文段。
填充字段 —— 这是为了使整个首部长度是 4 字节的整数倍。

## Slide 28: Chapter 6 Outline
6.1 Transport-layer services
6.2 Multiplexing and demultiplexing
6.3 Connectionless transport: UDP
6.4 Connection-oriented transport: TCP
  Segment structure
  Connection management
  Flow control
  Reliable data transfer
6.5 TCP congestion control

## Slide 29: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
Initialize TCP variables:
  Seq. #s
  Buffers, flow control info (e.g. RcvWindow)
Client: connection initiator
Socket clientSocket
= new Socket("hostname", "port number");
Server: contacted by client
Socket connectionSocket
= welcomeSocket.accept();
Notes: 建立连接的具体作用：使每一方确认对方的存在；双方协商一些参数，例如初始序号，初始接收窗口大小；资源分配

## Slide 30: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)

## Slide 31: Agreeing to establish a connection
2-way handshake failure scenarios:
retransmit
req_conn(x)
ESTAB
req_conn(x)
half open connection!
(no client!)
client terminates
server
forgets x
connection
x completes
retransmit
req_conn(x)
ESTAB
req_conn(x)
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x

## Slide 32: TCP Connection Management (Cont.)
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  Specifies client initial seq #
  No application data
Step 2: server host receives SYN, replies with SYNACK segment
  Server allocates buffers
  Specifies server initial seq. #
Step 3: client receives SYNACK, replies with ACK segment, which may contain data
client
Connection request (SYN=1 seq=client_isn)
server
Connection granted (SYN=1, seq=server_isn,
ACK (SYN=0, seq=client_isn+1)
ack=client_isn+1)
ack=server_isn+1

## Slide 33: TCP Connection Management (cont.)
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN
client
FIN
server
ACK
FIN
close
close

## Slide 34: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Note: with small modification, can handle simultaneous FINs
client
FIN
server
ACK
ACK
FIN
close
closing
closed
timed wait
closed
Notes: 参与TCP连接的两个进程中的任何一个都能终止该连接
Time wait时间是为了处理ACK丢失后客户端可重传最后的确认报文，所消耗的时间与具体实现有关。

## Slide 35: Exercises-1
1. Host A sends a TCP segment (SYN=1,seq=11220) to host B and expects to establish a TCP connection with host B. if host B accepts the connection request, the correct TCP segment sent by host B to host A may be ( )
SYN=0,ACK=0,seq=11221,ack=11221
SYN=1,ACK=1,seq=11220,ack=11220
SYN=1,ACK=1,seq=11221,ack=11221
SYN=0,ACK=0,seq=11220,ack=11220
Notes: 3

## Slide 36: Chapter 6 Outline
6.1 Transport-layer services
6.2 Multiplexing and demultiplexing
6.3 Connectionless transport: UDP
6.4 Connection-oriented transport: TCP
  Segment structure
  Connection management
  Flow control
  Reliable data transfer
6.5 TCP congestion control

## Slide 37: TCP Flow Control
Sender should not overwhelm receiver’s capacity to receive data
If necessary, sender should slow down transmission rate to accommodate receiver’s rate
Different from Congestion Control whose purpose was to handle congestion in network
But both congestion control and flow control work by slowing down data transmission
low capacity receiver
fast network
flow control problem

## Slide 38: TCP Flow Control
Receive side of TCP connection has a receive buffer:
Speed-matching service: matching the send rate to the receiving app’s drain rate
App process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control

## Slide 39: TCP Flow Control: How it Works
(Suppose TCP receiver discards out-of-order segments)
Spare room in buffer
= RcvWindow
= RcvBuffer-[LastByteRcvd - LastByteRead]
Rcvr advertises spare room by including value of RcvWindow in segments
Sender limits unACKed data to RcvWindow
  Guarantees receive buffer doesn’t overflow

## Slide 40: Technical Issue
Suppose RcvWindow=0 and that receiver has already ACK’d ALL packets in buffer
Sender does not transmit new packets until it hears RcvWindow>0
Receiver never sends RcvWindow>0 since it has no new ACKS to send to Sender
DEADLOCK!
Solution:
  TCP specs require sender to continue sending packets with one data byte while RcvWindow=0, just to keep receiving ACKS from receiver
  At some point the receiver’s buffer will empty and RcvWindow>0 will be transmitted back to sender

## Slide 41: Exercises-2
1. A TCP connection is established between host A and host B, and the MSS length of TCP is 1000 bytes. If the current congestion window of host A is 4000 bytes, after host A sends two MSS segments to host B continuously, host A successfully receives the confirmation segment of the first segment sent by host B, and the size of the receiving window in the confirmation segment is 2000 bytes, then the maximum number of bytes that host A can also send to host B is ( )
1000
2000
3000
4000
Notes: 1000

## Slide 42: Chapter 6 Outline
6.1 Transport-layer services
6.2 Multiplexing and demultiplexing
6.3 Connectionless transport: UDP
6.4 Connection-oriented transport: TCP
  Segment structure
  Connection management
  Flow control
  Reliable data transfer
6.5 TCP congestion control

## Slide 43: Reliable Data Transfer
Important in app., transport, link layers
Top-10 list of important networking topics!
Characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 44: Principles of reliable data transfer
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 45: Reliable Data Transfer: Getting Started
We’ll:
Incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
Consider only unidirectional data transfer
  But control info will flow on both directions!
Use finite state machines (FSM) to specify sender, receiver
state: when in this “state” next state uniquely determined by next event
state
1
state
2
event causing state transition
actions taken on state transition
event
actions

## Slide 46: Summary of the Protocols
Rdt1.0: all packets arrive correctly
Rdt2.0: all packets arrive, with possible errors only in data packets, and introducing ACK and NAK (no error)
Rdt2.1: corrupted ACKs/NAKs
Rdt2.2: similar to rdt2.1 remove NAKs
Rdt3.0: Allows packets to be lost and errors

## Slide 47: Rdt1.0: Reliable Transfer over a Reliable Channel
Underlying channel perfectly reliable
  No bit errors
  No loss of packets
Separate FSMs for sender, receiver:
  Sender sends data into underlying channel
  Receiver read data from underlying channel
packet = make_pkt(data)
udt_send(packet)
Wait for call from above
rdt_send(data)
sender
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
receiver

## Slide 48: Rdt2.0: Channel with Bit Errors
Underlying channel may flip bits in packet
  FCS/Checksum to detect bit errors
The question: how to recover from errors:
  Acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  Negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  Sender retransmits pkt on receipt of NAK
New mechanisms in rdt2.0 (beyond rdt1.0):
  Error detection
  Receiver feedback: control msgs (ACK,NAK) rcvr->sender
Notes: Flip 快速翻转，flip bits比特受损

## Slide 49: Rdt2.0: FSM specification
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for call from above
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
snkpkt = make_pkt(data, FCS/checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L

## Slide 50: Rdt2.0: Operation with No Errors
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
Wait for call from above
snkpkt = make_pkt(data, FCS/checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L
sender
receiver

## Slide 51: Rdt2.0: Error Scenario
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for call from above
snkpkt = make_pkt(data, FCS/checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 52: Rdt2.0 Has a Fatal Flaw!
What happens if ACK/NAK corrupted?
Sender doesn’t know what happened at receiver!
Can’t just retransmit: possible duplicate
Handling duplicates:
Sender retransmits current pkt if ACK/NAK garbled
Sender adds sequence number to each pkt
Receiver discards (doesn’t deliver up) duplicate pkt
Sender sends one packet,
then waits for receiver
response
stop and wait
Notes: Garbled:混乱的，引起误解的

## Slide 53
Sender: whenever sender receives control message it sends a packet to receiver
  A valid ACK: Sends next packet (if exists) with new sequence #
  A NAK or corrupt response: resends old packet
Receiver: sends ACK/NAK to sender
  If received packet is corrupt: send NAK
  If received packet is valid and has different sequence # as prev packet: send ACK and deliver new data up
  If received packet is valid and has same sequence # as prev packet, i.e., is a retransmission of duplicate: send ACK
Note: ACK/NAK do not contain sequence #

## Slide 54: Rdt2.1: Sender, Handles Garbled ACK/NAKs
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
L
Wait for call 0 from above
sndpkt = make_pkt(0, data, FCS/checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
sndpkt = make_pkt(1, data, FCS/ checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
Wait for
call 1 from above
Wait for ACK or NAK 1
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
L

## Slide 55: Rdt2.1: Receiver, Handles Garbled ACK/NAKs
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 56: Rdt2.1: Discussion
Sender:
Seq # added to pkt
Two seq. #’s (0,1) will suffice. Why?
Must check if received ACK/NAK corrupted
Twice as many states
  State must “remember” whether “current” pkt has 0 or 1 seq. #
Receiver:
Must check if received packet is duplicate
  State indicates whether 0 or 1 is expected pkt seq #
Note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 57: Rdt2.2: a NAK-free Protocol
Same functionality as rdt2.1, using ACKs only
Instead of NAK, receiver sends ACK for last pkt received OK
  Receiver must explicitly include seq # of pkt being ACKed
Duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 58: Rdt2.2: Sender, Receiver Fragments
sndpkt = make_pkt(0, data, FCS/checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for call 0 from above
Wait for ACK
0
sender FSM
fragment
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
L

## Slide 59: Rdt3.0: Channels with Errors and Loss
New assumption: Underlying channel can also lose packets (data or ACKs)
  Checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Q: how to deal with loss?
  Sender waits until certain data or ACK lost, then retransmits
  Any drawbacks?
Approach: sender waits “reasonable” amount of time for ACK
Retransmits if no ACK received in this time
If pkt (or ACK) just delayed (not lost):
  Retransmission will be duplicate, but use of seq. #’s already handles this
  Receiver must specify seq # of pkt being ACKed
Requires countdown timer

## Slide 60: Rdt3.0 Sender
sndpkt = make_pkt(0, data, FCS/checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
Wait for
call 0 from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
L
rdt_rcv(rcvpkt)
L
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
L

## Slide 61: Rdt3.0 In Action

## Slide 62: Rdt3.0 In Action

## Slide 63: Performance of rdt3.0
Rdt3.0 works, but performance stinks
Example: 1 Gbps link, 15 ms e-e prop. delay, 1KB packet:
T
transmit
=
8kb/pkt
109 b/sec
= 8 microsec
  U sender: utilization – fraction of time sender busy sending
L (packet length in bits)
R (transmission rate, bps)
=
  1KB pkt every 30 msec -> 33kB/sec thruput over 1 Gbps link
  Network protocol limits use of physical resources!
Notes: Stink:让人觉得很糟糕

## Slide 64: Rdt3.0: Stop-and-Wait Operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 65: Pipelined Protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  Range of sequence numbers must be increased
  Buffering at sender and/or receiver

## Slide 66: Pipelining: Increased Utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 67: Pipelined Protocols
Advantage: much better bandwidth utilization than stop-and-wait
Disadvantage: More complicated to deal with reliability issues, e.g., corrupted, lost, out of order data.
  Two generic approaches to solving this
    Go-Back-N protocols
    Selective repeat protocols

## Slide 68: GBN In Action

## Slide 69: Go-Back-N
Sender:
K-bit seq # in pkt header
“Window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  May receive duplicate ACKs (see receiver)
Timer for each in-flight pkt
Timeout(n): retransmit pkt n and all higher seq # pkts in window
Called a sliding-window protocol

## Slide 70: GBN: Sender
rdt_Send() called: checks to see if window is full
  No: send out packet
  Yes: return data to upper level
Receipt of ACK(n): cumulative acknowledgement that all packets up to and including n have been received. Updates window accordingly and restarts timer
Timeout: resends ALL packets that have been sent but not yet acknowledged.
  This is only event that triggers resend

## Slide 71: GBN: Sender Extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
base=1
nextseqnum=1
L

## Slide 72: GBN: Receiver Extended FSM
If expected packet received:
  Send ACK and deliver packet upstairs
If out-of-order packet received:
  Discard (don’t buffer) -> no receiver buffering!
  Re-ACK pkt with highest in-order seq #
  May generate duplicate ACKs
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L
Notes: If expected packet received:
  Send ACK and deliver packet upstairs
If out-of-order packet received:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK pkt with highest in-order seq #
  may generate duplicate ACKs

## Slide 73: More on Receiver
ACK-only: the receiver always sends ACK for last correctly received packet with highest in-order seq #
Receiver only sends ACKS (no NAKs)
Need only remember expectedseqnum
Can generate duplicate ACKs

## Slide 74
GBN is easy to code but might have performance problems
In particular, if many packets are in pipeline at one time (bandwidth-delay product large) then one error can force retransmission of huge amounts of data!
Selective Repeat protocol allows receiver to buffer data and only forces retransmission of required packets
Notes: .

## Slide 75: Selective Repeat In Action

## Slide 76: Selective Repeat
Receiver individually acknowledges all correctly received pkts
  Buffers pkts, as needed, for eventual in-order delivery to upper layer
Sender only resends pkts for which ACK not received
  Sender timer for each unACKed pkt
  Compare to GBN which only had timer for base packet
Sender window
  N consecutive seq #’s
  Again limits seq #s of sent, unACKed pkts
  Important: Window size < seq # range

## Slide 77: Selective Repeat: Sender, Receiver Windows

## Slide 78: Selective Repeat
Data from above :
If next available seq # in window, send pkt
Timeout(n):
Resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
Mark pkt n as received
If n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
Send ACK(n)
Out-of-order: buffer
In-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
Otherwise:
Ignore
receiver

## Slide 79: Selective Repeat: Dilemma
Example:
seq #’s: 0, 1, 2, 3
window size=3
Receiver sees no difference in two scenarios!
Incorrectly passes duplicate data as new in (a)
Q: what relationship between seq # size and window size?

## Slide 80: GBN vs. Selective Repeat
Selective repeat is more complicated as it needs buffering at the receiver, but only retransmit packets required for retransmission
GBN is simpler, but can lead to large number of unnecessary retransmission

## Slide 81: TCP Reliable Data Transfer
TCP creates rdt service on top of IP’s unreliable service
Pipelined segments
Cumulative acks
TCP uses single retransmission timer
Retransmissions are triggered by:
  Timeout events
  Duplicate acks
Initially consider simplified TCP sender:
  Ignore duplicate acks
  Ignore flow control, congestion control

## Slide 82: TCP sender (simplified)
wait
for
event
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
L
create segment, seq. #: NextSeqNum
pass segment to IP (i.e., “send”)
NextSeqNum = NextSeqNum + length(data)
if (timer currently not running)
start timer
data received from application above
retransmit not-yet-acked segment with smallest seq. #
start timer
timeout
if (y > SendBase) {
SendBase = y %cumulative acks
/* SendBase–1: last cumulatively ACKed byte */
if (there are currently not-yet-acked segments)
start timer
else stop timer
}
ACK received, with ACK field value y

## Slide 83: TCP Seq. #’s and ACKs
Seq. #’s:
  Byte stream “number” of first byte in segment’s data
ACKs:
  Seq # of next byte expected from other side
  Cumulative ACK: TCP only acknowledge bytes up to the first missing byte in the stream
Host A
Host B
Bytes [0~535]
Seq=XX1, ACK=536, data = ‘YYYY’
… …
Bytes [0~535], [900,1000]
Seq=XXN, ACK=536, data = ‘ZZZZ’
Q: how receiver handles out-of-order segments?
A: TCP spec doesn’t say, - up to implementer

## Slide 84: TCP: Retransmission Scenarios
Host A
Seq=100, 20 bytes data
ACK=100
time
premature timeout
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=92 timeout
ACK=120
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
time
Seq=92 timeout
SendBase
= 100
SendBase
= 120
SendBase
= 120
Sendbase
= 100

## Slide 85: TCP Retransmission Scenarios (more)
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
Cumulative ACK scenario
Host B
X
Seq=100, 20 bytes data
ACK=120
time
SendBase
= 120

## Slide 86: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
Longer than RTT
  But RTT varies
Too short: premature timeout
  Unnecessary retransmissions
Too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  Ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  Average several recent measurements, not just current SampleRTT

## Slide 87: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
Exponential Weighted Moving Average
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
Notes: exponential weighted moving average：EWMA,指数加权移动平均法，统计学观点，是指各数值的加权系数随时间呈指数式递减，越靠近当前时刻的数值加权系数越大。基本思想是加权平均对最近的样本赋予的权值要大于老样本的权重.采用该方法的理由：观察期的近期观察值对预测值有较大影响，它更能反映近期变化的趋势。相对于传统平均法的优势：一是不需要保存过去所有的数值，二是计算量显著减少。
EWMA 的表达式如下：
vt=βvt−1+(1−β)θtvt=βvt−1+(1−β)θt
上式中 θtθt 为时刻 tt 的实际温度；系数 ββ 表示加权下降的速率，其值越小下降的越快；vt 为 tt 时刻 EWMA 的值。
在 t=0时刻，一般初始化 v0=0 ，对 EWMA 的表达式进行归纳可以将 t 时刻的表达式写成：
vt=(1−β)(θt+βθt−1+...+βt−1θ1)vt=(1−β)(θt+βθt−1+...+βt−1θ1)
influence of past sample decreases exponentially fast：过去样本的影响以指数级的速度衰减
图中可见，sampleRTT在计算EstimatedRTT过程中趋于平缓

## Slide 88: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
estimate SampleRTT deviation from EstimatedRTT:
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
Notes: 除了估算RTT外，测量RTT的变化也是有价值的。考虑RTT的波动，估计EstimatedRTT与SampleRTT的偏差

## Slide 89: More on Sender Policies
Doubling the Timeout Interval
  Used by most TCP implementations
  If timeout occurs then, after retransmisison, Timeout Interval is doubled
  Intervals grow exponentially with each consecutive timeout
  When Timer restarted because of (i) new data from above or (ii) ACK received, then Timeout Interval is reset as described previously using Estimated RTT and DevRTT.
  Limited form of Congestion Control
Notes: 每一次TCP重传均将下一次超时间隔设为先前值的两倍
思考：这种思路和什么很相似？CSMA/CD中的二进制
如果TCP是一种停止等待协议，那么将超时间隔加倍就足以作为一种拥塞控制机制。然而，TCP使用流水线（因此不是停止等待协议），这允许发送方拥有多个未确认的未确认段。超时时间间隔的加倍不会阻止TCP发送方向网络发送大量首次传输的数据包，即使在端到端路径高度拥挤的情况下也是如此。因此，当出现网络拥塞迹象时，需要一种拥塞控制机制来阻止“从上述应用程序接收的数据”的流动。

## Slide 90: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs.
if sender receives “triple duplicate ACKs” for same data, resend unacked segment with smallest seq #
  likely that unacked segment lost, so don’t wait for timeout
TCP fast retransmit
Notes: RTT的这种机制可能会增加对丢包处理的时延，怎么办？

## Slide 91: TCP fast retransmit
X
fast retransmit after sender
receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data

## Slide 92: TCP ACK Generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap
Notes: 事件1：到达一个按序段，且前面的段都按需到达且确认，此时可以等一等，等是否可以背回或等下一个段到达然后一起确认，但最长等待时间不超过500ms
事件2：到达一个按序段，但前面一个还没确认，此时马上发单个累积确认，TCP协议要求每隔一个段就要发ACK
事件3：失序段到达，马上发累积确认，指示发送方重发
事件4：能填充间隔段到达，若该段起始于间隔的低端，立即发ACK

## Slide 93: TCP: GBN or Selective Repeat?
Basic TCP looks a lot like GBN
Many TCP implementations will buffer received out-of-order segments and then ACK them all after filling in the range
  This looks a lot like Selective Repeat
TCP is a hybrid

## Slide 94: Exercises-3
1. A TCP connection has been established between host A and host B. host A sends three consecutive TCP segments to host B, including 300 bytes, 400 bytes and 500 bytes payload respectively. The sequence number of the third segment is 900. If host B receives only the first and third segments correctly, the confirmation sequence number sent by host B to host A is( )
300
500
1200
1400
Notes: 500

## Slide 95: Chapter 6 Outline
6.1 Transport-layer services
6.2 Multiplexing and demultiplexing
6.3 Connectionless transport: UDP
6.4 Connection-oriented transport: TCP
  Segment structure
  Connection management
  Reliable data transfer
6.5 TCP congestion control

## Slide 96: Principles of Congestion Control
Congestion:
Informally: “too many sources sending too much data too fast for network to handle”
Different from flow control!
Manifestations:
  Lost packets (buffer overflow at routers)
  Long delays (queueing in router buffers)
A top-10 problem!
high capacity receiver
congested network
congestion control problem

## Slide 97: Approaches towards Congestion Control
End-end congestion control:
No explicit feedback from network
Congestion inferred from end-system observed loss, delay
Approach taken by TCP
Network-assisted congestion control:
Routers provide feedback to end systems
  Single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  Explicit rate sender should send at
Two broad approaches towards congestion control:
Notes: IBM的SNA、DEC的DECnet、TCP/IP、ATM等体系结构中采用让路由器用一个比特来指示网络中的拥塞情况，即显式地反馈网络拥塞状态

## Slide 98: Two Ways for Providing Feedback

## Slide 99: TCP Congestion Control
End-to-end control (no network assistance)
Transmission rate limited by congestion window size, Congwin, over segments
  Congwin dynamically modified to reflect perceived congestion
Tools are “similar” to flow control
sender limits transmission using:
LastByteSent-LastByteAcked  CongWin
How does sender perceive congestion?
loss event = timeout or 3 duplicate ACKs
TCP sender reduces rate (CongWin) after loss event
Notes: perceived congestion：所感知到的拥塞
TCP拥塞控制思路：让发送方根据所感知的网络拥塞程度，来限制其能向连接发送流量的速率
如何限制发送速率：设置拥塞窗口
如何感知网络拥塞：出现丢包事件
速率算法的改变：TCP拥塞算法

## Slide 100: TCP Congestion Control Algorithms
Three mechanisms:
  AIMD = Additive Increase Multiplicative Decrease
  Slow start = CongWin set to 1 and then grows exponentially
  Conservative after timeout events
Notes: Conservative 保守的

## Slide 101: TCP AIMD
Multiplicative decrease: cut CongWin in half after loss event
Additive increase: increase CongWin by 1 MSS every RTT in the absence of loss events: probing also known as congestion avoidance
Long-lived TCP connection

## Slide 102: TCP Slow Start
When connection begins, CongWin = 1 MSS
  Example: MSS = 500 bytes & RTT = 200 msec
  Initial rate = 20 kbps
Available bandwidth may be >> MSS/RTT
  Desirable to quickly ramp up to respectable rate
When connection begins, increase rate exponentially fast until first loss event
Slow Start is NOT really Slow!

## Slide 103: TCP Slow Start (more)
When connection begins, increase rate exponentially until first loss event:
  Double CongWin every RTT
  Done by incrementing CongWin for every ACK received
Summary: initial rate is slow but ramps up exponentially fast
one segment
RTT
two segments
Host A
Host B
time
four segments

## Slide 104
So Far
  Slow-Start: ramps up exponentially
  Followed by AIMD: sawtooth pattern
  Q: When should the exponential increase switch to linear?
Reality (TCP Reno)
  Introduce new variable threshold: initially very large
  Slow-Start exponential growth stops when reaches threshold and then switches to AIMD
  Two different types of loss events
    3 dup ACKS: cut CongWin in half and set threshold=CongWin (now in standard AIMD)
    Timeout: set threshold=CongWin/2, CongWin=1 and switch to Slow-Start

## Slide 105
Reason for treating 3 dup ACKS differently than timeout is that:
  3 dup ACKs indicates network capable of delivering some segments while
  Timeout before 3 dup ACKs is “more alarming”
Note that older protocol, TCP Tahoe, treated both types of loss events the same and always goes to slow-start with Congwin=1 after a loss event
TCP Reno’s skipping of the slow start for a 3-DUP-ACK loss event is known as fast-recovery

## Slide 106: Summary: TCP Congestion Control
When CongWin is below Threshold, sender in slow-start phase, window grows exponentially
When CongWin is above Threshold, sender is in congestion-avoidance phase, window grows linearly
When a triple duplicate ACK occurs, Threshold set to CongWin/2 and CongWin set to Threshold (only in TCP Reno)
When timeout occurs, Threshold set to CongWin/2 and CongWin is set to 1 MSS (TCP Tahoe does this for 3 Dup Acks as well)

## Slide 107: The Big Picture

## Slide 108: TCP Sender Congestion Control
Event | State | TCP Sender Action | Commentary
ACK receipt for previously unacked data | Slow Start (SS) | CongWin = CongWin + MSS, If (CongWin > Threshold) set state to “Congestion Avoidance” | Resulting in a doubling of CongWin every RTT
ACK receipt for previously unacked data | Congestion Avoidance (CA) | CongWin = CongWin+MSS * (MSS/CongWin) | Additive increase, resulting in increase of CongWin by 1 MSS every RTT
Loss event detected by triple duplicate ACK | SS or CA | Threshold = CongWin/2, CongWin = Threshold, Set state to “Congestion Avoidance” | Fast recovery, implementing multiplicative decrease. CongWin will not drop below 1 MSS
Timeout | SS or CA | Threshold = CongWin/2, CongWin = 1 MSS, Set state to “Slow Start” | Enter slow start
Duplicate ACK | SS or CA | Increment duplicate ACK count for segment being acked | CongWin and Threshold not changed

## Slide 109: Exercises-4
1. A TCP connection always sends TCP segments with 1KB MSS. The sender has enough data to send. A timeout event occurs when the congestion window is 16KB. If the transmission of TCP segments in the next four RTTS is successful, when all TCP segments sent in the fourth RTT receive positive responses, the size of the congestion window is( )
7KB
8KB
9KB
16KB
Notes: 9KB

## Slide 110: Chapter 6: Summary
Principles behind transport layer services:
  Multiplexing, demultiplexing
  Reliable data transfer
  Congestion control
Instantiation and implementation in the Internet
  UDP
  TCP

## Slide 111: Homework
P538:14,15
P322:27
P323:28
P326:42,43